## Slide 1: Department of Computer Science National Tsing Hua University
CS 5262: Multimedia Networking and Systems
Channel Modeling and Wide-Scale Internet Streaming Measurements
Instructor: Cheng-Hsin Hsu
Acknowledgement: The instructor thanks Prof. Mohamed Hefeeda at Simon Fraser University for sharing his course materials

## Slide 2: Outline
Channel Modeling
  Basic Probability Theory and Information Theory Concepts
  Discrete Memory-Less Channels (DMC)
  Channels with Memory
Internet Streaming Measurements

## Slide 3: Motivation
Why need model channels ?
  Help us to develop networked multimedia systems
  For example, different packet loss recovery mechanisms, such as retransmission, FEC, or both can be used in multimedia systems based on channel models
We cover basic channel models for multimedia packets

## Slide 4: Discrete Random Variable
Probability Mass Functions:
Joint Probability Mass Functions
Marginal Probability Mass Functions:
Independent Random Variables:
Conditional Probability Mass Functions:
Example of pmf for d.r.v X
Joint pmf for two r.v X and Y

## Slide 5: Entropy
Joint entropy
Conditional entropy (equivocation)
Entropy (uncertainty):
measure of the amount of uncertainty (randomness) associated with the value of the discrete random variable X
0 <= H(X) <= Log L ;
where X have L possible values

## Slide 6: Mutual Information
What is Mutual Information I(X; Y)?

## Slide 7: Mutual Information
Mutual information measures the information that X and Y share:
  How much knowing an r.v. reduces our uncertainty about the other one
Example:
  X and Y are indep.  knowing X does not give any information about Y and vice versa  I(X;Y)=0
  X and Y are identical  all information conveyed by X is conveyed by Y as well  I(X;Y)=I(X)=I(Y)
Some formulas:

## Slide 8: Channel Capacity
Shannon capacity
  Max amount of error-free data (information) that can be sent over a communication channel with a given bandwidth
  Theoretical max data rate over the channel
Defined as the maximum of the mutual information between the input and output of the channel
  Under input distributions
bits or packets per channel use
Notes: C= bits per channel use
B=channel uses per second
R=BC
R<=Min_i(Ri)=min_i(BiCi)

## Slide 9: Discrete Memoryless Channels DMC
P(Y|X)
  the probability of observing the output symbol Y given that we send the symbol X
The channel is said to be memoryless
  r.v. Y depends only on r.v. X at that time and is conditionally independent of previous X and Y
Communication system

## Slide 10: Binary Erasure Channel (BEC)
The input X: binary (Bernoulli) random variable (0 or 1)
: The loss (erased or deleted) probability
The output Y: ternary random variable (0,1 or erasure)

## Slide 11: Binary Erasure Channel (cont.)
No Error occur over a BEC: Pr[Y=0 | X=1] = Pr[Y=1 | X=0] = 0
This capacity, measured in “bits” per “channel use,” is achieved when the channel input X is a uniform r.v.
Notes: The expression for the capacity has some intuitive meaning: Since a proportion α of the bits are lost in the channel, we can recover (at most) a proportion 1 − α of the bits. Hence the capacity is at most 1 − α.
In many practical channels, the sender receives some feedback from the receiver. If feedback is available for the binary erasure channel, it is very clear what to do: If a bit is lost, retransmit it until it gets through.
Since the bits get through with probability 1 − α, the effective rate of transmission is 1 − α. In this way we are easily able to achieve a capacity of 1 − α with feedback.

## Slide 12: Packet Erasure Channel (PEC)
Multimedia packets  “bit-vectors”: bits of the same packet are either 100% received or erased
Inputs and outputs of PEC are r.v.’s
The capacity in this case is measured in “packets” per “channel use.”
is a binary random variable
Notes: Similarly, a cascade of L links of PEC channels has an effective
loss probability δ = 1 −%L i=1(1 − δi ) and end-to-end capacity C = 1 − δ = 1− (1 −%L i=1(1 −δi )) =%L i=1(1 −δi ) in packets per channel use.

## Slide 13: Cascaded BEC Channels
Consider two indep. BEC channels that are cascaded
The loss probability for the two channels could be different:
Capacity:
For L cascaded indep. BEC channels:
Channel capacity:

## Slide 14: Cascaded BEC Channels (cont.)
The end-end path of L BEC channels == a BEC channel with a loss probability:
The capacity C of the end-to-end route is bounded by the capacity Cmin (the smallest capacity among all channels).
  C ≤ Cmin = mini(Ci).
Notes: Cmin should not be confused by the “bottleneck” bandwidth Bmin, the bottleneck bandwidth usually represents the maximum transmission rate (e.g., 1.544 Megabits per second for a T1 line) that a particular link within the end-to-end path could support, and where this link has the minimum transmission rate: Bmin = mini(Bi ). Here, Bi can be thought of as the number of channel uses per second for link i. In general, a multimedia application must use a total rate Rtotal taking into consideration both the bottleneck bandwidth and the minimum end-to-end capacity. the effective (maximum) throughput of a BEC link i in terms of bits per second can be expressed as Ri = BiCi . Hence, the total rate Rtotal used by an application should be bounded by the following effective performance throughput: Rtotal ≤ mini(Ri ) = mini(BiCi ) in bits per second.

## Slide 15: The BEC Channel with Feedback
Channels may support some forms of feedback.
  For example, NACK for retransmission.
How to derive the performance bounds of such channels with feedback?
For any (DMC) Channel, feedback does not improve (or worsen for that matter) :
Discrete memoryless channel with feedback

## Slide 16: Cascaded BEC/PEC with Feedback
Feedback at end points:
Feedback link-by-link  the channel capacity is bounded by the capacity of a “bottlneck” link:
These are results for memoryless channels  channels with memory could increase their capacity by employing feedback!

## Slide 17: Packet Losses over Channel with Memory
Packet losses over Internet links and routes exhibit a high level of correlation and tend to occur in bursts  Channels with memory!
The most popular tool is Markov channels
A two-state Markov channel is the Gilbert–Elliott (GE) channel
  Good State (G) : the receiver receives all packets correctly
  Bad State (B) : all packets are lost

## Slide 18: Gilbert–Elliott Channel
    pGG = 1 - pGB and pBB = 1 – pBG
    The steady state probabilities :

## Slide 19: Recovery Probability
Probability of receiving i packets among n packets sent over GE channels
Extend the two-state GE model using the number of correctly received packets as the indexes (additional states)
Probability of sender sends n and receiver gets i packets == process starts at G0 or B0 and reaches Gi or Bi after n steps

## Slide 20: Recovery Probability and FEC
Detailed derivation can be found in [R. Howard, Dynamic Probabilistic Systems. Wiley, 1971].
Let φ(n, i) be the probability of sender transmits n packets and the receiver receives i packets:
Sample applications: for a (n,k) FEC coders, the decodable probability is:
Notes: An important performance measure for multimedia applications is the number
of packets received given that the transmitter sends n packets φ(n, i) . This measure, for example, could help application developers identify the level of resilience needed when transmitting a block of n video packets; this block of n packets may correspond to the number of packets in a Group of Pictures (GoP) of an MPEG stream. Another example could arise when the n packets may represent a Forward-Error-Correction (FEC) block with both k media data (e.g., video) packets and (n − k) parity packets that are used to recover lost packets within the n-packet FEC block

## Slide 21: Packet Correlation over Channels with Memory
Another way to set system parameters:
  The average loss p
  the packet correlation ρ, where:
The steady state probabilities:
ρ reveals how the states of two consecutive packets are correlated
  when ρ = 0, the loss process is memoryless (BEC)
  ρ increases  the states of two consecutive packets become more and more correlated.

## Slide 22: Packet Losses over Cascaded Channels with Memory
Close to the Internet  many routers with memory
The reception of i packets when transmitting n packets over two-cascaded channels with memory.

## Slide 23: Derivation of Probability (1/3)
The probability φ(n, i) of receiving i packets when the transmitter sends n packets into the first channel
That is,

## Slide 24: Derivation of Probability (2/3)
Since they are GE channels
Notes: Here, φj,G0Gi (n) (φj,B0Bi (n)) is the probability that the transmitter sends n
packets and the receiver receives i packets over the j th channel given that the channel begins and ends in a good (bad) state. Also, π(Gj ) (π(Bj )) is the probability that the j th channel is in a good (bad) state.

## Slide 25: Derivation of Probability (3/3)
Now for N channels with memory:
More compact version:

## Slide 26: Outline
Channel Modeling
  Basic Probability Theory and Information Theory Concepts
  Discrete Memory-Less Channels (DMC)
  Channels with Memory
Internet Streaming Measurements

## Slide 27: Goal
Use actual mutimedia streaming application to measure the network performance of the Internet
  More specifically with analog modems

## Slide 28: Previous Studies – TCP Perspective
Study the performance of the Internet
On backbone routers, campus networks
No studies represent how entertainment-oriented service will evolve
Ping, traceroute, UDP echo packets, multicast backbone audio packets

## Slide 29: Problem?
Not realistic! Do not represent what people experience at home when using real-time video streaming

## Slide 30: Study Real-Time Streaming
Use 3 different dial-up Internet Service Provider in the U.S.A.
Mimic their behaviour in the late 1990s-early 2000s
Real-Time streaming different than TCP because:
  TCP rate is driven by congestion control
  TCP uses an ACK for retransmission; real-time applications send an NACK which is different
  TCP relies on window-based flow control; real-time applications utilizes rate-based flow control

## Slide 31: Setup
Unix video server to the UUNET backbone with a T1
AT&T WorldNet, Earthlink, IBM Global Network
56kbps, V.90 modems
All clients were in NY state, but dialed long-distance numbers to every 50 states to connect, from various major cities in the U.S.A. To the ISP via PPP
Issue a parallel traceroute to the server and then stream a 10-min long video

## Slide 32: Setup (cont.)
Phone database of all numbers to dial
Dialer
Parallel Traceroute
  Implemented using ICMP (instead of UDP)
  Send all probes in parallel
  Record IP Time-to-live (TTL) for each returned messages

## Slide 33: Success Streaming Sessions
Sustain the transmission of the 10-minute video sequence at the stream's target IP rate r
Aggregate packet loss is less than a specific threshold
Aggregate incoming bit rate above a specific bit rate
Experimentally found that this filter-out modem-related (last-mile) issues

## Slide 34: When does the experiment end?
50 states (including AK and HI)
Each day separated into 8 chunks of 3 hours each
One week
50 x 8 x 7 = 2800 successful sessions per ISP

## Slide 35: Streaming Sequences
5 frames per second, encoded using MPEG-4
576-byte IP packet that always start at the beginning of a frame
Startup delay: network independant: 1300ms, delay jitter: 2700ms. Total: 4000ms

## Slide 36: Client-Server Architecture
Multi-threaded server, good for NACK requests
Bursts between 340 and 500ms for a low server overhead
Client uses NACK for lost packets
Client collects stats about received packets and decoded frames

## Slide 37: Notation
DXn for Dataset collected by ISPx (x = a, b, c) with Stream Sn (n = 1, 2)
Dn for the combined set {Dan U Dbn U Dcn}

## Slide 38: Experimental Results
D1
  3 clients performed 16,783 long-distance connections
  8429 successes
  37.7 million packets arrived at clients
  9.4 GB of data
D2
  17,465 connections
  8423 successes
  47.3 million packets arrived at clients
  17.7 GB of data

## Slide 39: Experimental Results (cont.)
Average time to measure an end-to-end path: 1731ms
D1 encountered 3822 different Internet routers; D2 4449 and together, 5266
D1 encountered on average 11.3 hops (from 6 to 17), 11.9 in D2 (from 6 to 22)

## Slide 40: Succesful Sessions
Time dependent

## Slide 41: Packet Loss
D1p average packet lost was 0.53%, D2p 0.58%
Much higher than what ISPs advertise (0.01 – 0.1%)
Therefore, suspect lost happens at the edges
38% of all sessions had no packet lost; 75% had loss rates < 0.3% and 91% rate lost < 2%
2% of all sessions have packet lost > 6%

## Slide 42: Packet Loss – Time Factor
Higher at rush hours

## Slide 43: Loss Burst Lengths
207,384 loss bursts and 431,501 lost packets  most of them are two packets

## Slide 44: Loss Burst Lengths (cont.)
In each of D1p and D2p:
  Single packet bursts contained 36% of all lost packets
  Bursts <= 2 contained 49%
  Bursts <= 10 contained 68%
  Bursts <= 30 contained 82%
  Bursts >= 50 contained 13%

## Slide 45: Loss Burst Durations
If a router's queue is full, and if packets are really close to one another within the burst, they might all be dropped
Loss-burst duration = time between the last packet received, and the one received after the burst loss
98% of loss-burst durations < 1second, which could be caused by data-link retransmission

## Slide 46: Heavy Tails
Packet losses are dependant from one another; it can create a cascading effect
Future real-time protocols should account for bursty loss packets, and heavy tail distribution
How to model it?

## Slide 47: Heavy Tails (cont.)
Paretto function
  CDF: F(x) = 1 – (β/x)α
  PDF: f(x) = αβαx-α-1
  In the case, α = 1.34 and β = 0.65

## Slide 48: Underflow Events
Packet loss: 431,501
159,713 (37%) were discovered missing when it was too late => no NACK
431,501 – 159,713 = 271,788 left
257,065 (94,6%) recovered before their deadline, 9013 (3.3%) were late and 5710 (2.1%) were never recovered

## Slide 49: Underflow Events (cont.)
Two types of late packets:
  Packets that arrive after the last frame of their GoP is decoded => completely useless
  Packets that are late, but can still be used for predicting frames within their GoP => partially late
Of the 9013 late retransmission, 4042 (49%) were partially late

## Slide 50: Underflow Events (cont.)
Total underflow by packet loss: 174,436
1,167,979 underflows in data packets, which were not retransmitted
1.7% of all packets caused underflows
Frame-freeze of 10.5s on average for D1p, and 8.6s for D2p

## Slide 51: Round-Trip Delay
660,439 RTT for each D1p and D2p
75% < 600 ms, 90% < 1 s, 99.5% < 10 s and 20 > 75 s

## Slide 52: Round-Trip Delay (cont.)
Depends on the time of the day
Correlated to the length of the end-to-end path (measured in hops with traceroute)
Very little correlation with geographical location

## Slide 53: Delay Jitter
One-way delay jitter = difference between one-way delay of 2 consecutive packets
Using positive values for one-way delay jitter, highest value was 45 s, 97.5% < 140 ms, and 99.9% < 1 s
Cascading effect: many packets can then be delayed, causing many underflows

## Slide 54: Packet Reordering
In Da1p, 1/3 missing packets was actually reordered
Frequency of reordering = % of reordered packets/total number of missing packets
In the experiment, this was 6.5% of missing packets, or 0.04% of all sent packets.
9.5% of sessions experienced at least one reordering
Independant of time of day and state

## Slide 55: Asymmetric Paths
Using traceroute and TTL-expired packets, can establish number of hops between sender and receiver
If number is different, definitely asymmetric
If the same, we don't know and call it potentially symmetric

## Slide 56: Asymmetric Paths (cont.)
72% of sessions were definitely asymmetric
Could happen because paths crosses over Autonomous Systems (AS) boundaries, where a “hot-potato” policy is enforced
95% of all sessions that had at least one reordering had asymmetrical paths
12,057 asymmetrical path sessions => 1522 had a reordering. 4795 possibly symmetric paths, only 77 had reordering

## Slide 57: Conclusion
Internet study for video streaming
Use various tools such as traceroute to know the routers along a path
Analyze the percentage of request that fail
Packet loss and loss-burst durations
Underflow events
Round trip delay
Delay jitter
Reordering and asymmetric paths