## Slide 1: Department of Computer Science National Tsing Hua University
CS 5262: Multimedia Networking and Systems
Digital Image Compression
Instructor: Cheng-Hsin Hsu
Acknowledgement: The instructor thanks Prof. Mohamed Hefeeda at Simon Fraser University for sharing his course materials

## Slide 2: Compression Methods
2
Audio, image, and video require huge storage and network bandwidth if not compressed
Example:
  10-min video clip (with no audio)
  30 frames per sec
  Frame resolution = 720 pixels x 480 pixels
  Bits per pixel = 8 x 3 = 24
  Video file size ~= 17.4 GB
  Bandwidth required for streaming > 240 Mb/s
Notes: 2

## Slide 3: Types of Compression
3
Lossless Compression: no information is lost
  Run-Length Encoding (RLE)
  Entropy Encoding
    Shannon-Fano, Huffman
  Arithmetic Encoding
Lossy Compression: some (unimportant) information is lost
  E.g., frequencies not heard in audio, subtle details not noticed in image  high compression ratios
Notes: 3

## Slide 4: Run-Length Encoding
4
Idea: consider the following pixel values
  255, 255, 255, 255, 240, 240, 240, 150, 150, 150
RLE (value, repetition): (255,4), (240, 3), (150, 2)
Size of compressed string?
  Value: needs 8 bits (ranges from 0 to 255)
  Repetition: depends on the longest run in the image
  Assume repetition takes 8 bits for the above example 
  Compression ratio = (10 x 1 byte ) / (3 x 2 bytes) = 1.67
RLE used in image/video compression
  Usually there are rows of pixels with same color
  Or rows of zero AC coefficients
RLE may increase size in some situations!
  255, 255, 240, 210 (255, 2), (240,1), (210,1)  ratio = 4/6=0.67
Notes: 4

## Slide 5: Entropy Encoding
5
Entropy of information source S generating symbols is:
  pi : probability of symbol i appearing
Entropy measures the degree of randomness (uncertainty) of symbols generated by the source
  S always generates same specific symbol  H(S) = 0
  H(S) increases as uncertainty increases, max when all symbols are equally likely to appear
Shannon showed that:
  The minimum average number of bits needed to represent a string of symbols equals to its entropy
Notes: 5

## Slide 6: Entropy Encoding: Examples
6
Ex1: image with 256 pixels, each with different color 
  pi = 1/256 for i = 0,1,2, …, 255  Entropy = 8
  That is, average #bits to encode each color is 8 (cannot do better)
Ex2: image with 256 pixels, with the following
  Entropy = 2.006  min avg #bits to represent a color
  We can achieve this by assigning different #bits (codes) to different colors (variable length encoding)
Huffman and Shannon-Fano algorithms approximate this
Color | Freq | pi | Min #bits
black | 100 | 0.391 | 1.356
white | 100 | 0.391 | 1.356
yellow | 20 | 0.078 | 3.678
orange | 5 | 0.020 | 5.678
red | 5 | 0.020 | 5.678
purple | 3 | 0.012 | 6.415
blue | 20 | 0.078 | 3.678
Notes: 6

## Slide 7: Huffman Algorithm
7
Variable Length Encoding:
    Fewer number of bits for more frequent colors
  Prefix-free code:
    No ambiguity during decoding  space saving (otherwise, we need either length field or terminating sequence)
  Two passes:
    Determine the codes for the colors
      Compute frequencies
      Build Huffman tree (bottom up)
      Assign codes (top down)
    Replace each color by its code
Notes: 7

## Slide 8: Huffman Algorithm: Example
8
Image with five colors
Huffman tree
Notes: 8

## Slide 9: Huffman Algorithm: Example (cont’d)
9
Assigning codes top down
Decoding
  Need frequencies (or the tree)
  Bits from the compressed file are matched (left=0 & right=1) from root down
Note: each color needs integer number of bits, although the optimal (according Shannon) may be fractional 
Arithmetic Encoding
Notes: 9

## Slide 10: Arithmetic Encoding
10
Avoids the disadvantage of Huffman encoding
  Comes closer to the optimal
  Still uses statistical analysis (entropy coding)
It encodes a whole string of symbols in one floating point number
  Each symbol is assigned a probability interval with size proportional to its frequency of occurrence
The code (floating point number) of a sequence of symbols is created by successively narrowing the range between 0 and 1 for each symbol
Notes: 10

## Slide 11: Arithmetic Encoding: Example
11
100 pixels with frequencies 
Consider encoding 6 pixels: W K K Y R B
  W: interval 0.4 – 0.65
  K: interval 0 – 0.4 of the W’s interval
  And so on …
Color | Frequency | Probability Interval
black (K) | 40/100 = 0.4 | 0–0.4
white (W) | 25/100 = 0.25 | 0.4–0.65
yellow (Y) | 15/100 = 0.15 | 0.65–0.8
red (R) | 10/100 = 0.1 | 0.8–0.9
blue (B) | 10/100 = 0.1 | 0.9–1.0
Notes: 11

## Slide 12: Arithmetic Encoding: Example
12
Encoding of W K K Y R B
Notes: 12

## Slide 13: Arithmetic Encoding: Example
13
Decoding:
  Assume final number (code) is 0.43137
  Falls in W’s interval  first symbol is W
  Subtract low value of W’s interval and scale by its width  (0.43137 – 0.4)/0.25 = 0.12548
  which is in K’s interval  second symbol is K
  … and so on
Notes: 13

## Slide 14: Arithmetic Encoding: Notes
14
Form of entropy encoding
But gives closer to optimal results (more compression) than Huffman encoding
Can be done using only integer operations
IBM and other companies hold patents on algorithms for arithmetic encoding
Used in recent video coding standards (H.264/AVC)
Notes: 14

## Slide 15: JPEG Compression
15
Divide image into 8 × 8 pixel blocks
Convert image to luminance/chrominance model, e.g., YCbCr
  Optional; could apply same algorithm on each of the R, G, B components
Apply 2d DCT
  Shift pixel values by -128 (makes image more centered around 0)
Quantize DCT coefficients
Store DC value (upper left corner) as the difference between current DC value and DC from previous block
Do run-length encoding
  in zigzag order
Do entropy encoding, e.g., Huffman
Store file in standard format (header contains info for decoder, e.g., quantization tables, Huffman codes, …)
Notes: 15

## Slide 16: Chroma Subsampling
Eye is more sensitive to changes in light (luminance) than in color (chrominance)  subsample CbCr
Subsampling notation: a:b:c
  From 4 x 4 block: take a samples from Y; b samples from each of Cb & Cr from top row; and c samples from each of Cb & Cr from bottom row
  Common examples: 4:1:1; 4:2:0; 4:2:2
  Ex: 4:2:0 yields a saving of (16 * 3) / (16 + 4 * 2) = 2

## Slide 17: Subsampling and Macroblocks
With subsampling (i.e., if YCbCr is used), we create 8 x 8 blocks as follows:
  Divide the image into 16 x 16 macroblocks
   four 8 x 8 blocks for Y (no subsampling for Y)
  #of blocks for CbCr depends on the subsampling
  E.g., 4:2:0 & 4:1:1  one block for Cb & one for Cr
Y
Y
Y
Y
Cb
Cr
S
16 x 16
S
16 x 16
S
16 x 16

## Slide 18: Quantize DCT Coefficients
Uniform Quantizer: Divide each coefficient by integer and round
  The only lossy operation in the whole compression algorithm
    Larger integers  Larger compression AND larger distortion/error
  High frequency coefficients are usually small  become zeros  more compression
  Quantization Table
    Each coefficient could have a different quantizer
    Larger quantizers for high frequency coefficients
uint_8 luminance_quant_tbl[DCTSIZE2]={
16, 11, 10, 16, 24, 40, 51, 61,
12, 12, 14, 19, 26, 58, 60, 55,
14, 13, 16, 24, 40, 57, 69, 56,
14, 17, 22, 29, 51, 87, 80, 62,
18, 22, 37, 56, 68, 109, 103, 77,
24, 35, 55, 64, 81, 104, 113, 92,
49, 64, 78, 87, 103, 121, 120, 101,
72, 92, 95, 98, 112, 100, 103, 99
};
u_int8 chrominance_quant_tbl[DCTSIZE2]={
17, 18, 24, 47, 99, 99, 99, 99,
18, 21, 26, 66, 99, 99, 99, 99,
24, 26, 56, 99, 99, 99, 99, 99,
47, 66, 99, 99, 99, 99, 99, 99,
99, 99, 99, 99, 99, 99, 99, 99,
99, 99, 99, 99, 99, 99, 99, 99,
99, 99, 99, 99, 99, 99, 99, 99,
99, 99, 99, 99, 99, 99, 99, 99
};

## Slide 19: Run-length Encoding
Done in zigzag order
  sorts values from low-frequency to high frequency components 
  longer strings of 0’s (because high frequency components are usually 0)
Important: Work out the complete example in [Sec 3.1, Burg09]

## Slide 20: Summary
Lossless compression: RLE, Entropy, Arithmetic
Lossy compression: ignores less important info to achieve higher compression ratios
Chroma subsampling: take fewer samplers from colors
  de-emphasize color components because eyes are more sensitive to luminance
  E.g., 4:2:2  4 samples Y, 2 samples CbCr each from even row, 2 samples CbCr from odd rows
JPEG compress
  Blocks  convert to YCbCr  DCT  Quantize  zigzag RLE  Entropy coding