## Slide 1: Department of Computer Science National Tsing Hua University
CS 5262: Multimedia Networking and Systems
Media On Demand and Live Broadcast
Instructor: Cheng-Hsin Hsu
Acknowledgement: The instructor thanks Prof. Mohamed Hefeeda at Simon Fraser University for sharing his course materials

## Slide 2: Introduction
2
Media on demand
  Playback audio or video
  Control over start time, and other interactive controls
Live Broadcast
  Tuning in to a radio or TV program
  Limited control (join / leave)
Both scenarios exist today on the internet
Notes: 2

## Slide 3: Outline
3
Introduction
Multimedia Architecture, Protocols, and Files Formats
Live Broadcast
Fundamental Abstractions
Streaming Media over Packet Networks
Notes: 3

## Slide 4: Architectures
Streaming Media on Demand
Media source
Media is encoded off line
File format to support streaming
Streaming Protocols
“Client Buffer”
Relatively long
network jitter compensation
error recovery …
Only to buffer relatively large decoded frames
Multimedia over IP and Wireless Networks. Pg 454, Fig 14.1 (a)

## Slide 5: Architectures
Streaming Media on Demand
  The entire file is available on the server (flexibility)
  “progressive downloading” is possible
    Maximum download speed, real time playback speed.
    Large client buffer
    Limited buffer devices can use TCP flow control.
  Only when network bandwidth > source coding rate
Multimedia over IP and Wireless Networks. Pg 454, Fig 14.1 (a)

## Slide 6: Architectures
Live broadcast
  NOT possible:
    to allow VCR-like control for clients.
    to adapt one transmission rate for a particular client.
    to use retransmission-based error control.
Limited buffer
minimize end-to-end delay
Multimedia over IP and Wireless Networks. Pg 454, Fig 14.1 (b)

## Slide 7: Outline
7
Introduction
Architectures
  Media on Demand
  Live Broadcast
Communication Protocols
File Formats
Live Broadcast
Notes: 7

## Slide 8: Communication Protocols
Many protocols, at different levels
  Content discovery
  Auxiliary files, content description
  Streaming control protocol
  Data transfer protocol
  Transmission rate control
  Error control

## Slide 9: Communication Protocols
Content discovery
  Usually through URLs
  Typically have a form such as http://www.microsoft.com/directory/contentname.asx http://www.realnetworks.com/directory/contentname.ram http://www.apple.com/directory/contentname.mov
Adobe. Streaming Media Primer. Pg 37.

## Slide 10: Communication Protocols
ASX Meta Files (basic) <ASX version="3.0”> <ENTRY> <REF HREF="Path"/> </ENTRY> </ASX>
Microsoft. Introduction to Windows Media Metafiles. 2004.

## Slide 11: Communication Protocols
ASX Meta Files (advance)
  Ad Insertion
  Server or Protocol rollover
  <ASX version="3.0”> <ENTRY>
  <REF HREF="http://sample.microsoft.com/BallGame" />
  </ENTRY>
  <EVENT NAME="TimeOut" WHENDONE="RESUME">
  <ENTRY CLIENTSKIP="NO">
  <REF HREF="http://Server/Content/Advert.asf" />
  </ENTRY>
  </EVENT>
  </ASX>
  <ASX version="3.0”> <ENTRY>
  <REF HREF="rtsp://Server1/Path/File1.asf"/>
  <REF HREF="mms://Server2/Path/File1.asf"/>
  <REF HREF="http://WebServer/Path/File1.asf"/>
  </ENTRY>
  </ASX>

## Slide 12: Communication Protocols
Streaming Protocol
  High-level control protocol to enable the client to interactively control playback using VCR-like functions.
  Commands are sent over TCP
  Real Time Streaming Protocol (RTSP)
    HTTP-like protocol
    Basic control commands
    Extension for dynamic selections

## Slide 13: Communication Protocols
Adobe. Streaming Media Primer. Pg 17.

## Slide 14: RTSP Commands
Multimedia over IP and Wireless Networks. Pg 459, Table 14.1
(Dynamic stream / protocol selection)

## Slide 15: Communication Protocols
Data transport protocol
  Real-time Transfer Protocol (RTP)
    RTP over UDP , RTP over TCP
    Standardized with RTSP
    Preferred for bandwidth efficiency
    RTP over UDP : error & transmission rate control  the application!
  HTTP over TCP
    Avoid firewall issues
    Appropriate only for playback (e.g. YouTube)

## Slide 16: RTSP Commands
Adapted from W3C. Ret 2010
SDP
RTCP
  Real Time Control Protocol
    - Usually paired with RTP.
    - Provide statistical feedback to the sender.

## Slide 17: Communication Protocols
RTP over UDP: Windows Media system
  Transmission Rate Control
    constant bit rate transmission at the source coding rate
    client monitors its buffer for congestions
    signal to the sender to switch the coding rate down
    absence of congestion can raise up the rate again
  Error control
    Selective retransmission (gaps in sequence)
    Highest priority: Audio packets
    Lowest priority: Video packets closest to the deadline
    stall if lost audio packets – skip lost video packets.

## Slide 18: File Formats
Media on Demand
  Encoder cannot predict network & clients conditions
    must consider flexibility in files.
    adaption is left to the server in real time conditions.
  Raw (uncompressed) files?
    the file  huge storage space needed.
    real-time encoding  high computational complexity
  Less extreme:
    high bit rate encoding for file’s content
    online transcode / recompress content for each client.
  Opposite end!  no adaptation
    Fixed encoding. Simply copied onto network connection.

## Slide 19: File Formats
Better engineering:
  Maintain flexibility. Provide indexing for contents.
Streaming file formats
  MPEG-4 - Apple’s QuickTime
  RealNetworks’ RealMedia - Microsoft’s ASF
  Common Characteristics
    Contain multiple version of each medium.
    Each version is recorded in a track.
    Each track is decomposed into a sequence of chunks.
    Chunks contain actual media data.
    header structures in each file contain static metadata
      relate to overall file as well as to specific tracks.

## Slide 20: File Formats
Metadata
  Title, author, date of composition, encryption, copyrights, table of contents…
  track enumeration, relationships…
  Individual track properties: start time, duration, bit rate, buffer size, sampling rate…
  Time-varying metadata associated with each track: e.g. network packetization info, SMPTE time codecs…
    Differences between formats in how these metadata are associated with individual chunks.

## Slide 21: File Formats
Media data
  Only appropriate subset of the data to be transmitted.
  Subset selection : coarse-grained or fine-grained
  Coarse-garined
    Per-stream basis
    Change on a timescale > data unit
  Fine-grained
    Selection at the data unit level
    Also portion of each data unit can be selected.

## Slide 22: File Formats
Source coding rate control
  Multibit rate (MBR): independent streams
  Scalable coding: enhancement layers
Transmission
  After the selection of data units, they are prepared for transmission
    Packetization: re-encapsulate the encoded media data from one transport protocol (the file format) into another (e.g. RTP).

## Slide 23: MPEG-4 File Format
- Structures “atoms”
- Unique tag & length
- Atoms are in moov
- Data can be in mdat
or referenced via URL
MPEG-4 Overview. ISO/IEC JTC1/SC29/WG11 (2002). Fig 13 & 14.

## Slide 24: Hint Tracks & Indexing
  Indexing to allow seeking in each track (search efficiency)
  Fixed length records unit of time (e.g. 1-s interval)
  Each record contains a pointer into each track
MPEG-4 Overview. ISO/IEC JTC1/SC29/WG11 (2002). Fig 16.

## Slide 25: MOV File Format
- Highly Extensible
- Unique codes & GUIDs
- Extensions must be understandable by servers and clients to use it
- Static metadata: transmitted.
- Indexing info: not transmitted.
Apple QuickTime File Format. Ret 2001.

## Slide 26: Outline
26
Introduction
Multimedia Architecture, Protocols, and Files Formats
Live Broadcast
Fundamental Abstractions
Streaming Media over Packet Networks
Notes: 26

## Slide 27: Live Broadcast
Major issue: heterogeneity across clients in
  Channels
    Error control & bit rate
  Devices
    Resolution
    Computational power
    Single encoding is not sufficient!
Apple QuickTime. Ret 2010

## Slide 28: Live Broadcast: bit rate adaption
Simulcast
  E.g. simultaneously broadcasting standard definition and HD TV.
  Analogues to multibit rate files.
  Simulcast streams with different bit rates, error protection, source resolution, and decoding requirements.
  Clients tune in to the appropriate channel
Layered Multicast
  Based on scalable coding
  Each layer is multicast to different address
  Client subscribe/unsubscribe from the topmost enhance layer
  More efficient.

## Slide 29: Live Broadcast: error control
Packet retransmission?
  Limitation on feedback to the server
  Timely feedback (ACK or NACK)  feedback implosion
  Does not scale to large numbers of clients
Statistical feedback
  E.g. RTCP
  Client: average packet-loss rate
  Server: understand clients population. Tailor streams.
Protection
  Forward Error Correction (FEC)
  Priority Encoded Transmission (PET) (scalable)

## Slide 30: PET packetization
Multimedia over IP and Wireless Networks. Pg 492, Fig 14.12
Layers
Layer K is protected
(N, K) RS code
Any K out of N packets
received can recover the first K layers.

## Slide 31: PET quality
Multimedia over IP and Wireless Networks. Pg 493, Fig 14.13
Zero packets
received
8 out of 8 packets received

## Slide 32: Error & Bit rate controls
Error Protection (FEC or PET) with
  Simulcast (straight forward)
    Apply FEC or PET on each stream with a certain bit rate.
  Layered multicast
    Insufficient protection of a lower layer will render a higher layer irrelevant.
    The lower layers need more error protection than the higher layers.
    New enhancement layer  add more protection to preceding layers.

## Slide 33: Conclusion
Media on Demand
  More flexibility in protocols, error, and transmission control.
  Use standard protocols to ensure interoperability.
  Streamable file formats: flexible, extensible, and provide easy access to required contents.
Live Broadcasting
  Biggest challenge in heterogeneous clients and real time requirements.
  Combine protection from errors with variable bit rate coding for efficient use of resources.

## Slide 34: Outline
34
Introduction
Multimedia Architecture, Protocols, and Files Formats
Live Broadcast
Fundamental Abstractions
Streaming Media over Packet Networks
Notes: 34

## Slide 35: Context for Fundamental Abstractions
Context:
  The Internet is not reliable
  We assume it is reliable in our discussion
  Focus is on buffering and transmission of encoded signals
  Encoding and Decoding assumed to be instantaneous
Goals:
  Understand fundamental abstractions of streaming media on demand
  Understand Leaky Bucket models for idealized bit streams
  Understand when it is safe for a client to begin playback
  Understand terms: CBR vs VBR Streams, Preroll Delay, Timestamps

## Slide 36: Buffering and Leaky Bucket Models
Communication Pipeline
Constant Bit Rate (CBR) Transmission
Variable Bit Rate (VBR) Transmission
Buffer Tubes
Leaky Buckets

## Slide 37: Communications Pipeline
Point A – captured frames instantaneously encoded and put into the encoder buffer
Point B – when bits enter the communication channel
Point C – when bits leave the communication channel
Point D – when frames removed from decoder buffer and instantaneously decoded
On-Line Streaming Models:
  Isochronous (synchronous) noiseless communication channel
  Encoder constant bit-rate transmission rate over the channel
  Instantaneous source coding rate
To match encode/decode rates to transmission rate:
Encoding Buffer required between Encoder and the Channel
Decoding Buffer required between Channel and the Decoder
I call it rate regulation!
MULTIMEDIA OVER IP AND WIRELESS NETWORKS, pg 465 FIGURE 14.3

## Slide 38: Constant Bit Rate (CBR) Media Streams
Used by On-Line Media on Demand Streaming when:
  Constrained by maximum transmission bit rate
  Consistent bit-rate more important than Quality
Encoder uses Quantization Control to control bit rate of Encoded stream
Quantization Control
Quantization Control

## Slide 39: Coded Bit Stream Schedules
Coding Schedule: Sequence of times at which successive bits in the coded bit stream pass a given point in the communications pipeline
  Schedule A – Staircase function which increases by b(n) bits at time T(n)
  Schedule B – when bits enter the communication channel with slope R bits/second
  Schedule C – when bits leave the communication channel with slope R bits/second
  Schedule D – when frames removed from decoder buffer and instantaneously decoded
MULTIMEDIA OVER IP AND WIRELESS NETWORKS, pg 465 FIGURE 14.4

## Slide 40: Coded Bit Stream Schedules (cont.)
MULTIMEDIA OVER IP AND WIRELESS NETWORKS, pg 465 FIGURE 14.4
Gap between A and B represents, at any point in time, the number of bits in encoder buffer
Gap between B and C is transmission delay
Gap between C and D represents, at any point in time, the number of bits in decoder buffer
Line A and D are the same shaped line  defined by frame sizes
Line B is the lower bound to schedule A (if A goes slower than B, buffer will empty)  Underflow
Line C is upper bound to schedule D (D can’t go any faster than C)  Overflow

## Slide 41: Buffer Tube contains a Coding Schedule
MULTIMEDIA OVER IP AND WIRELESS NETWORKS, pg 466 FIGURE 14.5
Buffer Tube: Contains the source coding schedule (line A or D)
Encoder uses a “rate control” algorithm to assign number of bits b(n) to each frame to maintain buffer within Tube
Resultant Bit Stream is called a CBR bit stream with average rate R
Used by On-Line source encoder to ensure output will not cause decoder to overflow/under-run buffer  called HRD model in H.264/SVC

## Slide 42: Buffer Tube contains a Coding Schedule (cont.)
MULTIMEDIA OVER IP AND WIRELESS NETWORKS, pg 466 FIGURE 14.5
Buffer Tube characterized by three parameters (R, B, Fd)
  Slope R = transmission speed in bits/second
  Height B = Capacity in bits of each buffer (end-to-end delay = B/R seconds)
  Fd = Number of bits in decoder buffer before it starts presenting the data (Fd = B – Fe) (delay Dd = Fd/R)
  Fe = Number of bits in encoder buffer before it starts transmitting the data (delay De = Fe/R)

## Slide 43: Selecting the best Buffer Tube
Infinite number of buffer tubes can contain a finite-duration bit stream
  Slope R, width B, and offset Fe are not unique
  Lower channel bit rate R can be accommodated with more buffering B
Selecting the best Buffer Tube, select slope R:
  with tightest fit to stream’s schedule {(b(n), T(n))}
  with average bit rate = (Total Number of Bits)/(Duration of Bit Stream)
MULTIMEDIA OVER IP AND WIRELESS NETWORKS, pg 467 FIGURE 14.6

## Slide 44: Preroll Delay
Decoder buffer delay Dd also referred to as Preroll Delay
  Typically largest component of start up delay for Streaming Media on Demand
  For off-line source encoding, encoder delay not important
  Focus is on decoder buffer delay Dd = Fd/R only
  trade-off between reduced preroll delay and initial frame quality
  See 14.4 for more details
Also called initial buffering delay

## Slide 45: Variable Bit Rate (VBR) Streams
VBR
Jordi Ribas-Corbera [2], pg 675 FIGURE 2
CBR
Jordi Ribas-Corbera [2], pg 674 FIGURE 1
  VBR Used for producing Media Stream with constant distortion for consistent quality
  Can not maintain constant bit rate using QC to control encoded frame size b(n)
  A VBR steam model is a generalization of the CBR stream model:
  Both CBR and VBR have schedules with finite sequences of frame sizes over time
  Both can be contained in Buffer Tubes with the appropriate (R, B, Fd)
  VBR requires wider Buffer Tube than for equivalent CBR stream
  VBR requires larger preroll delays than CBR due to variability in bit rate
  - allows the decoder to have more bits in its buffer to prevent decoder buffer under-run

## Slide 46: Leaky Bucket
Extend model to case where encoder does not use channel continuously
Peak transmission rate R higher than average bit rate of stream
When encoder has bits to send, it sends them at rate R, idle otherwise
More realistic model for packet networks
Modelled as a Leaky Bucket: (R, B ,Fe)
Encoder dumps b(n) bits into leaky bucket at time T(n)
Bits leak out of the bucket and into the channel at rate R
Bucket has capacity B and initial fullness of Fe bits
Be(n): Encoder buffer fullness after frame n added to buffer
Fe(n): Encoder buffer fullness before frame n added to buffer
Given initial Leaky Bucket Fullness Fe before bit transmission starts,
The system can be modelled as:

## Slide 47: The Tightest Leaky Bucket
A leaky bucket (R, B, Fe) is said to contain a bit stream with schedule
{(b(n), τ(n))}
if the bucket does not overflow, that is, Be(n) ≤ B for all n = 0, 1, . . . , N
For a given stream, want the Tightest Leaky Bucket which contains it.
Define minimum bucket capacity given leak rate R and initial fullness Fe as:
Define the corresponding initial decoder buffer fullness as:
Denote the minimum of each of these over Fe as:
Each is minimized by the same value of Fe which is equal to:
Denote the minimum of each of these over Fe as:
Define the corresponding initial decoder buffer fullness as:

## Slide 48: Leaky Bucket Parameters as a function of R
Buffer size Bmin depends on Bucket Leak Rate R
  For R < Rc, larger and larger buffers are required
  For R >> Rc, buffers seldom filled and few required
For off-line encoding of media on demand,
  Value of R used by client often differs from source coding rate Rc
  Encoder pre-computes required buffer size and preroll delay for various values of R
  Pre-computed values for various R can be stored in header as (R, Bmin, Fd) triplets
MULTIMEDIA OVER IP AND WIRELESS NETWORKS, pg 470 FIGURE 14.7
Rc = 600Kbps

## Slide 49: Compound Streams
Streaming Media files often contain multiple independent streams
  Audio Stream
  Video Streams
Leaky bucket for aggregate stream:
  Derived as sum of leaky buckets containing each component stream
  Will contain the combined stream, but not strictly the tightest possible
Given:
  Audio stream with leaky bucket (Ra, Ba, Fa)
  Video stream with leaky bucket (Rv, Bv, Fv)
Compute aggregate stream leaky bucket as follows:

## Slide 50: Temporal Coordinate Systems
Media time refers to clock running on capture device
  Monotonically increasing timestamps of the original content
  One second of media time elapses in one second of real time
Client time t refers to playback time at client
  Time of media playback at client
  Content may be played back at different values of V
    V < 1 for Slow-Motion
    V = 1 for PLAY
    V > 1 for Fast-Forward
Conversion from media time to client time:

## Slide 51: Timestamps
Decoder timestamp (DTS)
  arrival deadline for decoding the frame at the client
  Provides decoding dependency order for P and B Frames
Presentation timestamp (PTS)
  Tells renderer when to render and present the frames
  Useful for synchronizing concurrent streams
Decoder and Presentation order can differ
  Presentation Order: I0B1B2P3B4B5P6
  Decoding Order: I0P3B1B2P6B4B5

## Slide 52: Conclusions
Media on Demand streams modelled by Encoder using Buffer Tubes
Leaky Bucket model more appropriate for transmission over packet networks
Leaky Bucket parameters can be summed for aggregate streams
Preroll Delay a function of Buffer requirements and Transmission Rate R

## Slide 53: Backup

## Slide 54: Component Streams with Multiple Leaky Buckets
Given La audio and Lv video leaky buckets:
There are (La x Lv) possible pairs but only (La + Lv) pairs are of interest.
They lie on lower convex hull of set used to compute Bemin(R) & Fdmin(R)
Indices for pairs easily found by minimizing the Lagrangian for some positive Lagrange multiplier λ>0 :
Chose La audio leaky buckets by minimizing the Lagrangian:
Chose Lv video leaky buckets by minimizing the Lagrangian:
Pair up Audio and Video leaky buckets with same λ

## Slide 55: MBR and Scalable Streams
MBR adds choice of streaming from set of mutually exclusive media streams, each with a different coding rate.
Scalable Streams similar to compound streams except must chose sets of layers.
Lots of combinations! Most are not useful.
Choose based on selecting a desired distortion level versus bit rate.
For each combined stream (i,j), define an over-all distortion and source rate:
Select a “desirable” subset of audio/video combinations (i,j) such that:
  Di,j ≤ Di’,j’ for all (i’,j’) such that Ri’,j’ ≤ Ri,j
As with compound streams, use Lagrangian method to find desirable pairs.