## Slide 1: SDN Tutorial

## Slide 2: SDN Tutorial
Topics:
Prerequisites
Create topology, Modify topology
Simple switch, Add flow
Packet-in handler, Packet-out
Packet filter in packet-in handler
Add actions to push, pop MPLS labels
Multiple tables

## Slide 3: Prerequisites
Required tools and versions:
  Open vSwitch 2.3.0
  Mininet 2.1.0p
  Ryu 3.17
Install:
  Please follow the instruction in files under SDN_Tutorial/Installation to install the OpenvSwitch, Mininet, and Ryu

## Slide 4: Terminology
Terminology | Open vSwitch | OpenFlow | Ryu
Switch | Bridge | OpenFlow Switch | Datapath
Port | Port/Interface | OpenFlow Port | Port
Flow Entry | Flow/Flow Entry | Flow Entry | Flow Entry

## Slide 5: Task 1
Topics: Create topology, Modify topology
Using tool: Mininet

## Slide 6: Task1 – Mininet Custom Topology
topo-2sw-2host.py (by mininet)
  The source code is in Mininet’s source tree: mininet/custom/topo-2sw-2host.py
To start up a mininet with the custom topology
  sudo mn --custom topo-2sw-2host.py --topo mytopo --controller remote
  Use ‘exit’ to close the mininet
h1
h2
s1
s2

## Slide 7: Task1 – Read topology from JSON and create it
mytopo.py (in Exercise_1)
  A sample code modified from mininet custom topology
  Read topology description from json file then use custom topology to create it
Run mytopo.py:
  sudo mn --custom mytopo.py --topo mytopo --switch ovsk --controller remote --mac --link tc
h1
h2
e1
e2
s1
s3
s2
h3
e1
e1
e3
e2
e1
e2
e1
e1
the port number of node
The topology in sample file

## Slide 8: Task1 – Options in mininet command (mn)
Switch type:
  --switch=ovsk
    Use openvswitch kernel switch
  --switch=user
    Use openvswitch user-space switch
  --custom=CUSTOM
    Read custom topo and node params from .pyfile
  --mac
    Automatically set host MACs for hosts
  --controller=remote
    Connect to remote controller (Default IP is 127.0.0.1)
  --link tc
    Use tc link in mininet (Set bandwidth, delay, jitter, loss… for links)
Type “mn –help” to see more

## Slide 9: Task1 – Topology JSON file
Define “node” and “link” in topology
node:
  The node name in mininet
link:
  “src”: the src node of this link
  “dst”: the dst node of this link
  “bw”: the bandwidth of this link
  “delay”: the delay value of this link
  “p1”: the port number of src node
  “p2”: the port number of dst node
{"node": [ "s1", "s2", "s3", "h1", "h2", "h3"],
"link": [
{"src": "h1", "dst": "s1", "bw": 10, "delay": "100ms", "p1": 1, "p2": 2},
{"src": "h2", "dst": "s2", "bw": 10, "delay": "100ms", "p1": 1, "p2": 2},
{"src": "h3", "dst": "s3", "bw": 10, "delay": "100ms", "p1": 1, "p2": 3},
{"src": "s1", "dst": "s3", "bw": 10, "delay": "100ms", "p1": 1, "p2": 1},
{"src": "s2", "dst": "s3", "bw": 10, "delay": "100ms", "p1": 1, "p2": 2}
]}
h1
h2
e1
e2
s1
s3
s2
h3
e1
e1
e3
e2
e1
e2
e1
e1

## Slide 10: Exercise1 – Modify JSON file and create a new topology
Modify topo_sample.json to create a new topology like the following picture
Assign the port number for each interface
Type ‘net’ in mininet to show your topology
h1
h2
h3
h4
s1
s2
s3
s4

## Slide 11: Task 2
Topics: Simple switch, Add flow
Using tools: Ryu, tcpdump(wireshark), ovs-vsctl & ovs-ofctl

## Slide 12: Task2 – Simple switch in Ryu
Material:
  The switch hub implementation tutorial in Ryu book (Please read it and follow the execution steps.) http://osrg.github.io/ryu-book/en/html/switching_hub.html#id1
The source code of simple switch is in Ryu’s source tree: ryu/app/simple_switch_13.py

## Slide 13: Exercise2 – Add flow
Delete the function “_packet_in_handler” and modify the function “switch_features_handler” in simple_switch_13.py (start from exercise2.py)
After finishing the installation of table-miss flow on switches, add flow-entries to build up the communications between h1 and h3 in exercise1’s topology.
h1
h2
h3
h4
s1
s2
s3
s4

## Slide 14: Exercise2 - Hints
Hint1: You need to add 2 flow-entries on s1 and s3
  Ex: (for s1)
    Flow1: Forward packets from port X to port Y
    Flow2: Forward packets from port Y to port X
Hint2: Flow’s attributes match: inport, actions: outport, priority=1
  (priority=0 is table-miss flow)
Hint3: Use datapath.id to get switch index
h1
h2
h3
h4
s1
s2
s3
s4
ex:
match = parser.OFPMatch(in_port=2)
actions = [parser.OFPActionOutput(1)]
self.add_flow(datapath, 1, match, actions)
x
Y

## Slide 15: Task 3
Topics: Packet-in handler, Packet-out
Using tool: Ryu

## Slide 16: Exercise3 – Packet-in handler
Modify the function “_packet_in_handler” in simple_switch_13.py (start from exercise3.py)
Use topology in exercise1. Similar to exercise2, use packet-out to forward packets between h1 and h3.
h1
h2
h3
h4
s1
s2
s3
s4

## Slide 17: Exercise3 - Hints
Hint1: Add “--arp” when running mininet to let the hosts get the mac addresses of other hosts
Hint2: Use mac address dst (destination) to decide the outport of switch
h1
h2
h3
h4
s1
s2
s3
s4
ex:
if dst == '00:00:00:00:00:01':
actions = [parser.OFPActionOutput(1)]
out = parser.OFPPacketOut(datapath=datapath, buffer_id=msg.buffer_id,
in_port=in_port, actions=actions, data=data)
datapath.send_msg(out)

## Slide 18: Task 4
Topic: Add filter in packet-in handler
Using tool: Ryu

## Slide 19: Exercise4 – Packet-in filter
Modify the function “_packet_in_handler” in simple_switch_13.py (start from exercise4.py)
Use ethertype to identify different types of captured packets and print their src and dst (IP packets and ARP packets)
  Material: Ryu Packet library API Reference http://ryu.readthedocs.org/en/latest/library_packet_ref.html
Exercise4(a): Do not use ‘--arp’ in mininet to automatically learn mac addresses on hosts, and use ping to generate ARP packets
Exercise4(b): Use ‘--arp’ in mininet to automatically learn mac addresses on hosts, and use ping to gernerate ICMP packets (IP type)

## Slide 20: Exercise4 - Hints
Hint1: You need the library in Ryu’s source code
  Find the required field of protocols in the library
from ryu.ofproto.ether import ETH_TYPE_IP, ETH_TYPE_ARP
from ryu.lib.pacekt import ipv4, arp

## Slide 21: Task 5
Topic: Add actions to push, pop MPLS labels
Using tool: Ryu

## Slide 22: Exercise5 – Add MPLS actions
Delete the function “_packet_in_handler” and modify the function “switch_features_handler” in simple_switch_13.py (start from exercise5.py)
After finishing the installation of table-miss flow on switches, add flow-entries to build up the communications between h1 and h3 in exercise1’s topology.
Similar to exercise2, but use MPLS label to distinguish packets between switches.
  Push and pop MPLS label on edge switch
Use user-space switch(in ovs, kernel switch do not support MPLS)
  sudo mn --custom mytopo.py --topo mytopo --switch ovsk,datapath=user --controller remote --mac --link tc
h1
h2
h3
h4
s1
s2
s3
s4

## Slide 23: Exercise5 - Hints
Hint1: Required match and actions
  Push:
  Pop:
match = parser.OFPMatch(eth_type=ETH_TYPE_IP,
eth_dst='00:00:00:00:00:03')
actions = [datapath.ofproto_parser.OFPActionPushMpls(ETH_TYPE_MPLS),
datapath.ofproto_parser.OFPActionSetField(mpls_label=10),
datapath.ofproto_parser.OFPActionOutput(2)]
match = parser.OFPMatch(eth_type=ETH_TYPE_MPLS,
mpls_label=30)
actions = [datapath.ofproto_parser.OFPActionPopMpls(ETH_TYPE_IP),
datapath.ofproto_parser.OFPActionOutput(1)]

## Slide 24: Task 6
Topic: Multiple tables
Using tool: Ryu

## Slide 25: Task6 – Multiple tables
Use multiple tables to implement pre-build flows of MPLS path
Find some paths beforehand and assign them with MPLS labels. When the traffic comes, add flows to match certain MAC addressed on edge switches.
Use instruction to adjust actions

## Slide 26: Exercise6 – Pre-build flows
After finishing the installation of table-miss flow on switches, add flows to match certain MPLS labels.
Add flows: (ex: for the path from s1 to s3)
  (on s1): table 10, match: label 10, actions: output, instruction: apply actions
  (on s3): table 0, match: label 10, actions: pop mpls label, instruction: apply actions, goto table 10
h1
h2
h3
h4
s1
s2
s3
s4
(table 10)
label 10
(table 10)
label 30

## Slide 27: Exercise6 – Traffic comes
When switches get ARP or IP packets from h1 or h3 to each others, add flows to push MPLS label
Add flows: (ex: for the path from s1 to s3)
  (on s1): table 0, match: dst:0x03, actions: push label 10, instruction: apply actions, goto table 10
  (on s3): table 10, match: dst:0x03, actions: outport 1, instruction: apply actions
h1
h2
h3
h4
s2
s3
s4
label 10
label 30

## Slide 28: Exercise6 - Hints
Hint1: for flow with lower table-id, use instructions to go to another table Material: https://github.com/osrg/ryu-book/blob/master/en/source/openflow_protocol.rst
Hint2: Add parameter of table_id and instruction in function “add_flow”
ex:
instruction = [parser.OFPInstructionActions(datapath.ofproto.OFPIT_APPLY_ACTIONS, actions),
parser.OFPInstructionGotoTable(10)]
def add_flow(self, datapath, table_id, priority, match, instruction, actions, buffer_id=None):
ofproto = datapath.ofproto
parser = datapath.ofproto_parser
inst = instruction
mod = parser.OFPFlowMod(datapath=datapath, priority=priority,
match=match, table_id=table_id, instructions=inst)
datapath.send_msg(mod)

## Slide 29: Exercise6 - Hints
Hint3: Use self.dpset to get datapath structure in Ryu
  self.dpset = { dpid: datapath structure of dpid }
  ex: to get dpid 1
datapath = self.dpset[1]