## Slide 1: A Load-Balanced Video Multicast Routing System in Software-Defined Networks
Meng-Wei Lee 李孟葳
2015/10

## Slide 2: Outline
Motivation
System Overview
Problem Formulations & Proposed Solutions
Testbed
Experiments in Mininet
Conclusion

## Slide 3: Motivation
Video streams dominate the Internet traffic:
  IP video traffic will be 80% of all IP traffic by 2019, up from 67% in 2014 [1]
Usage scenarios
  (a) Video surveillance networks
  (b) Video conferencing services
[1] Cisco visual networking index: Forecast and methodology, 2014-2019

## Slide 4: Motivation (cont.)
Real-time streaming imposes strict Quality of Service
  Requirements on connections of latency, packet loss rate, and bandwidth …
How to reduce redundant streams and video bandwidth requirements?

## Slide 5: Current Solution
IP multicast
  Complex operation – IGMP, PIM, MOSPF, and DVMRP
  Need costly devices
Streaming Server
Client
Computers

## Slide 6: Our Solution
Software-Defined Networks (SDNs)
Controller
Switches

## Slide 7: Successful Case
Google's SDN (OpenFlow) WAN (2010 - 2012)
Source: Google

## Slide 8: Successful Case
Google's SDN (OpenFlow) WAN (2010 - 2012)
Source: Google

## Slide 9: Benefits of Using SDNs
Centralized multicast routing algorithm
Lower network overhead
Lower setup cost and maintenance cost
Streaming Server
Client
Computers
Controller
Switches

## Slide 10: Related Work
Multicast in SDNs
  [37] proposes a multi-party video conferencing system
  [20] focuses on customizing the multicast services
  They only discuss the performance of existing multicast routing algorithms
  We design the centralized multicast routing algorithms, which aims to balance the load among the network links
  Utilize Multiple Description Coding (MDC) for robust multipath multicast routing
[37] M. Zhao, B. Jia, M. Wu, H. Yu, and Y. Xu., “Software defined network-enabled multicast for multi-party video conferencing systems,” in Proc. of IEEE International Conference on Communications (ICC’14), Sydney, Australia, June 2014
[20] S. Liao, X. Hong, C. Wu, B. Wang, and M. Jiang. “Prototype for customized multicast services in software defined networks,” In Proc. of IEEE Software, Telecommunications and Computer Networks (SoftCOM’14), Split, Croatian, September 2014

## Slide 11: Multiple Description Coding (MDC)
Separate a frame into several descriptors
Any subset of descriptors can be decoded
Transmitted over separate channels
Provide error resilience to media streams
An image transmitted in 4 descriptors by MDC
(a) 4 descriptors received
(b) Descriptor #3 is lost
Quality improves while more descriptors received
(a)
(b)
BARNETT, Eran; KASPI, Yoni. Multiple Description Image Coding. 2005.

## Slide 12: Design Objectives
Multipath multicast routing system in SDNs
  Robustness
  Load Balancing
  Adaptation
  Reliability
  SDN Compatible

## Slide 13: Outline
Motivation
System Overview
Problem Formulations & Proposed Solutions
Testbed
Experiments in Mininet
Conclusion

## Slide 14: System Overview
Client
Computers
Streaming
Server
Switches
Controller
OF Control Channel
IP-in-IP Tunnel
Multicast Management
Topology Monitor
ARP Proxy
Forwarding Agent
Algorithms
Multicast Routing
Application
Multicast
Tree
Multicast
Request

## Slide 15: Outline
Motivation
System Overview
Problem Formulations & Proposed Solutions
Testbed
Experiments in Mininet
Conclusion

## Slide 16: Problem Formulation - Objective
We consider the network topology as a directed graph
Objective:
Minimize the maximal link utilization
x=1, if the link is one of
the multicast tree edge
bandwidth of the link
A switch, a source, or a sink
A network link between two vertices
link utilization

## Slide 17: Problem Formulation – Constraints
  1. For each vertex
  - Limit the number of
  ﬂow-entries
  2. For each edge
  - The traffic flow must be less
  than its bandwidth
  3. For each video
  - To be robust, a switch
  can participate in up to
  multicast trees

## Slide 18: Robust Multipath Multicast Routing
It is an Integer Programming (IP) problem
We use IBM CPLEX to solve the optimal solution of network load balancing
The solution may contain cycles

## Slide 19: Cycle Elimination
Whenever the cycle occurs
  Add more constraints to the formulation
  Save more time rather than prevent cycle in advance
Optimal solution of multipath multicast trees
Abbreviated as RMMR*
  Optimal Robust Multipath Multicast Routing Algorithm
But it is still time consuming in large networks
  Need a more efficient solution!

## Slide 20: Route Adaptation Heuristics
Only modify a part of multicast trees for sinks join/leave
  RMMR: Efficient Robust Multipath Multicast Routing Algorithm
  Call RMMR* for optimal multicast trees first
  Run above heuristics to update multicast trees
function LEAVE(video sink , video )
for all descriptor = 1,2,… do
loop switches from to the root of tree
reduce the count of down-stream video sinks
remove the switch with 0 count from tree
Sink leaves
function JOIN(video sink , video )
for all descriptor = 1,2,… do
perform BFS from for the shortest path to tree
add the shortest path with minimal link utilization to tree
Sink joins
Heuristic:

## Slide 21: Robust Multipath Multicast Routing Algorithms
  RMMR*
    Optimal Robust Multipath Multicast Routing Algorithm
  RMMR
    Efficient Robust Multipath Multicast Routing Algorithm

## Slide 22: Outline
Motivation
System Overview
Problem Formulations & Proposed Solutions
Testbed
Experiments in Mininet
Conclusion

## Slide 23: Testbed Setup
4 OpenFlow switches – Pica8 P3297
1 OpenFlow controller - Ryu
1 video source - VLS
3 video sinks - VLC
2 video streams represent 2 descriptors

## Slide 24: Testbed

## Slide 25: Higher Link Utilization Causes Longer Latency
Average packet latency increases about 0.4 sec while link congestion
Link bandwidth: 10 Mbps
We stream two 4 Mbps videos from source

## Slide 26: Our System Incurs Short Response Time
2.5 ms
Report:
0.071 sec
Leave:
0.084 sec
Flow insertion time ranges from 1 to 4.5 ms
IGMP messages response time ranges from 0.023 to 0.15 sec

## Slide 27: Outline
Motivation
System Overview
Problem Formulations & Proposed Solutions
Testbed
Experiments in Mininet
Conclusion

## Slide 28: Experiments in Mininet
Link bandwidth: 1~5 Mbps
Algorithm comparison
  - RMMR* - optimal
  - RMMR - heuristic
  - IPM - IP multicast
  (PIM-SM)
Topology | Switch | Source | Sink | Descriptor
Small | 9 | 1 | 6 | 2
Large | 24 | 4 | 12 | 4

## Slide 29: Experiment Setup
MDC video traces and their bit rates:
  - Mobile 1.22 Mbps
  - Hway 0.27 Mbps
  - Paris 0.5 Mbps
  - Tempete 0.91 Mbps
We conduct 10-min experiments with RMMR*,RMMR, and IPM
The sink join/leave rates = 2 (sinks/minute)
MDC video traces from ASU

## Slide 30: Our Algorithms are Bandwidth-aware
Large bit rate videos get higher frame loss rates using IPM
Our algorithms result in almost zero frame loss rate
Mobile
Max
Mean
Min

## Slide 31: Our Algorithms Achieve Higher Video Quality
Gaps between RMMR(*) and IPM with
Mobile (4 dB) and Tempete (1 dB)
IPM leads to at most 10 dB quality fluctuation

## Slide 32: Our Algorithms Reduce Max Link Utilization
Reduce max link utilization
up to 50%
Reduce max link utilization 20~30%
Max
Mean
Mobile
30%
50%

## Slide 33: Our Proposed Algorithms are Robust Against Switch Failures
We shutdown switch 1 at 65 sec
Our system recovers the routes in few seconds after switch failure

## Slide 34: The Scalability of Our Algorithms
RMMR always terminates in < 0.2 sec
Running Time
Running Time

## Slide 35: Tradeoff Between Optimality and Running Time
RMMR* has higher optimality:
Reduce max link utilization up to 6%
RMMR is more efficient:
Reduce running time from 8 sec to 50 ms
6%
8 sec
50 ms
Running Time

## Slide 36: Outline
Motivation
System Overview
Problem Formulations & Proposed Solutions
Testbed
Experiments in Mininet
Conclusion

## Slide 37: Conclusion
Multicast on SDNs
  Reduce setup cost and maintenance cost
  Use a global view to get an optimal solution for multicast routing
RMMR(*) algorithm
  Robust, load balanced, and flexible
  RMMR*: Optimal solution, suitable for smaller and more static networks
  RMMR: Efficient solution, suitable for larger and more dynamic networks

## Slide 38: Future Work
Consider background traffic to compute the multicast routing depends on the current traffic
Design an adaptive algorithm, which automatically makes decisions on when to update the multicast routing with optimal solution

## Slide 39
Thank you！

## Slide 40
Specialized Packet Forwarding Hardware
Feature
Feature
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Operating
System
Operating
System
Operating
System
Operating
System
Operating
System
Network OS
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Source: ONF Slides
Software-Defined Networks
Traditional
Networks
Software-Defined
Networks
Control Data Plane Interface
(e.g., OpenFlow)

## Slide 41: SDN Multicast Related Work
M. Zhao, B. Jia, M. Wu, H. Yu, and Y. Xu., “Software defined network-enabled multicast for multi-party video conferencing systems,” in Proc. of IEEE International Conference on Communications (ICC’14), Sydney, Australia, June 2014
  Proposed a multicast multi-party system in SDNs and discuss the performance of existing multicast routing algorithm.
S. Liao, X. Hong, C. Wu, B. Wang, and M. Jiang. “Prototype for customized multicast services in software defined networks,” In Proc. of IEEE Software, Telecommunications and Computer Networks (SoftCOM’14), Split, Croatian, September 2014
  Focused on customizing the multicast services and only discuss the performance of existing multicast routing algorithms
  We propose, implement the multicast system in SDNs and design the centralized multicast routing algorithms to balance the overhead among the network links.

## Slide 42: SDN Multicast Related Works (cont.)
Iyer, A.; Kumar, P.; Mann, and V., "Avalanche: Data center Multicast using software defined networking," in Proc. of IEEE Communication Systems and Networks (COMSNETS’14), Bangalore, India, January 2014
  Proposed algorithm to minimize the size of multicast tree and increase the path diversity to avoid congestion.
L.-H. Huang, H.-J. Hung, C.-C. Lin, and D.-N. Yang. “Scalable and bandwidth-efficient multicast for software-defined networks,” In Proc. of IEEE Global Communications Conference (GLOBECOM’14), Austin, USA, December 2014
  Proposed a Branch Aware Edge Reduction Algorithm for multicast routing for SDNs.
Complementary to the existing OpenFlow-related multicast research, our proposed algorithm utilizes MDC for robust multipath multicast routing among multiple video sources and sinks

## Slide 43: SDN Multicast Related Works (cont.)
K. A. Noghani and M. Oguz Sunay. “Streaming multicast video over software-deﬁned networks.” in Proc. of IEEE Mobile Ad Hoc and Sensor Systems (MASS’14), Philadelphia, USA, October 2014
  Distributed the multicast videos with Multiple description coding and leverage the benefits of MDC, which provide potential of lower link utilization and better error resilience in transmission.
We also leverage the centralized view of SDNs to design the optimal and its corresponding heuristic to improve the multicast routing algorithms for load balancing

## Slide 44: Challenges on Multipath Routing
The benefits of using multipath
  Fault tolerance
  Increased bandwidth
Drawback
  If the client can not receive the data in time, the rest portion of video would be useless

## Slide 45: System Overview
Client
Computers
Streaming
Server
Switches
Controller
OF Control Channel
IP-in-IP Tunnel
Multicast Management
Topology Monitor
ARP Proxy
Forwarding Agent
Algorithms
Multicast Routing
Application
Multicast
Path
Multicast
Request

## Slide 46: Design Objectives
Multipath multicast routing algorithm in SDNs
  Robustness
    Provide high video quality even in unstable networks
  Load balancing
    Avoid network congestion
  Adaptation
    Dynamically adapt to network changes
  SDN Compatible
    Complying the limit of OpenFlow switches
  Reliability
    Route recovery while network failure

## Slide 47: Problem Formulation - Notation
We consider a video multicast system and modeled it as a directed graph
Our problem is to compute the multicast trees for optimal min-max load balancing
A source, a sink or a switch
A network link between two vertices

## Slide 48: Problem Formulation – Constraints (cont.)
Ensure that video sources and sinks are indeed the roots and leaves of the multicast trees
Allow the intermediate vertices to avoid receiving duplicated descriptors from multiple links
Ensure that a vertex sends a descriptor only if it’s received
Ensures that a vertex must send a descriptor once it’s received

## Slide 49: Problem Formulation – Constraints (cont.)

## Slide 50: SDN Architecture
Source: SDN White Paper

## Slide 51: System Architecture

## Slide 52: Outline
Motivation
System Overview
Problem Formulations & Proposed Solutions
Implementation
Testbed
Experiments in Mininet
Conclusion

## Slide 53: Implementation
Multipath multicast routing system
  Ryu
    Component-based framework
  OpenFlow 1.3

## Slide 54: Component Diagram
multicast packet-in/IGMP packet-in
ARP packet-in
IP packet-in

## Slide 55: Component Diagram
ARP packet-in
LLDP packet-in/ARP packet-in

## Slide 56: Component Diagram

## Slide 57: Testbed Result

## Slide 58: Link Utilization and Latency
Short latency while link utilization is low
Link bandwidth: 10Mbps
Two 3Mbps videos

## Slide 59: RMMR(*) Algorithms Result in Consistent Throughput
Max
Mean
Min
Throughputs in RMMR(*) are all around video bitrates.
Max
Mean
Mobile
In IPM, some sinks get duplicated packets, some sinks lose lots of packets.
1.22
0.89
0.5
0.2

## Slide 60: The Scalability of RMMR(*) Algorithms

## Slide 61: Tradeoff of Optimality in Different Periodical Parameter
p: the periodical parameter to regularly update the multicast routes with optimal solution
Update optimal solution more frequently results in less link utilization but costs more time

## Slide 62: Future Work
Consider background traffic to compute the multicast routing depends on the current traffic
Design an adaptive algorithm, which automatically makes decisions on when to update the multicast routing with optimal solution