## Slide 1: Mobile Cloud Offloading on Crowdsensing Platforms
Ting Yi Lin

## Slide 2: Outline
Introduction
  Efficient Crowdsensing System With Offloading
  Offloading Applications To Cloud
  Contributions
Offloading Applications To Cloud
  Architecture
  Problem Statement
  Algorithm
  Experiments
Offloading Event Analysis Algorithms: Using IsCrowded And IsNoisy As Case Studies
  Implementation
  Case Studies
  Evaluations
Conclusion And Future Work

## Slide 3: Population of Mobile Device, Wireless Network, and Cloud Platform
Mobile devices are more and more popular
  Smart phone, tablet, etc
  1.75 billion smartphone users (2014)[1]
Wireless network coverage
  The number of access points and the bandwidth are increasing
Provide service to user through the network
[1] http://www.emarketer.com/Article/Smartphone-Users-Worldwide-Will-Total-175-Billion-2014/1010536
Notes: Recent year, mobile device is more and more popular. The mobile devices, such as smart phone and tablet can see in everywhere and becomes an important part of our life. We can run applications as we do on desktop but it is portable, you can bring them anywhere with you.

## Slide 4: What Is Crowdsensing ?
Smartphones are now equipped with multiple sensors
  GPS, accelerometer, microphone, gyroscope, etc.
The crowds provide useful information for each others
  Events are detected through processing the sensory data
Ask questions
Answer questions or provide sensor data

## Slide 5: Why Is Crowdsensing Interesting?
It has many applications
It has many advantages
  Users can ask questions which are hard for algorithms to answer
  Improving the coverage of traditional sensor networks
  Lowering the deployment and maintenance cost for companies

## Slide 6: What Is The Most Efficient Execution Flow?
Most of the crowdsensing systems analyze the sensory data on broker/server
  It is not efficient
  The computation capability and network bandwidth of servers and mobiles are different
Offloading is a good solution
Network Type | Wifi | 3G | Local
Current (mA) | 9.2619 | 285.3662 | 24.0448
Time (ms) | 224.99 | 3559.85 | 299.34

## Slide 7: Mobile Cloud Offloading
Mobile devices has limited resources
  CPU, memory, GPU, battery lifetime, etc.
  Cannot run resource-intensive applications
Cloud service can be used to address on the issue
  Cloud servers have large amount of resources
  Can be accessed easily through network
  Using powerful server to do the heavy computations
Light Computations
Mobile
Heavy Computations
Cloud
Send Heavy Tasks To Cloud
Get Results From Cloud
Notes: So, we know that mobile device has limited computation resources. Such as the cpu capability, memory space, battery lifetime and so on. The limited resources make the mobile device may surfer from the user response delay or impossible for running some computation-intensive tasks. The battery lifetime is also a big problem for users.
relative to the mobile device, the cloud server has abundant computation resources and can easily accessed through network. As you can imagine, the cloud servers let us have a chance to improve the application performance and longer the battery lifetime.
Such a technique is called Offloading, that is, we offload (or you can say migrate) the tasks on mobile device to a more powerful cloud server. Using the cloud server’s computation resources to do the computation for the mobile device.

## Slide 8: Contributions
We propose an offloading decision algorithm [MCC’13]
We develop an APK analysis tool to analyze and modify APK files
We offload existing third-party applications to show offloading is feasible in existing applications
We integrate offloading into a crowdsensing prototype system to show the performance gain from offloading [PIMRC’14]

## Slide 9: Outline
Introduction
  Efficient Crowdsensing System With Offloading
  Offloading Applications To Cloud
  Contributions
Offloading Applications To Cloud
  Architecture
  Problem Statement
  Algorithm
  Experiments
Offloading Event Analysis Algorithms: Using IsCrowded And IsNoisy As Case Studies
  Implementation
  Case Studies
  Evaluations
Conclusion And Future Work

## Slide 10: Architecture
Notes: Describe what is decision engine

## Slide 11: System Execution Flow
Method A
Method B
Decision
Application
No
Cloud
Method B
Yes
Database
Store the local execution cost
Store the cloud execution cost

## Slide 12: Why We Need A Decision Engine?
Offloading cannot always improve performance or reduce energy consumption
  Transmission energy computation energy
Many factors can affect the offloading efficiency
  Wireless connectivity, mobile CPU usage, etc.
We aim to minimize the energy consumption on mobile device or improve the application performance
  We should carefully determine whether to offload
Notes: Though offloading can save energy or reduce the execution time, it is not always true. Why it don’t work under some circumstances? It is because if we want to use the cloud server to do the computation, we need to transmit the code, input data, and program state. It intuitive that if the transmission energy is larger than the computation energy, offloading cannot save energy and even consume more energy on transferring the computation.
There are many factors that can affect the offloading efficiency, such as wireless connectivity, cpu usage and so on.
In order to determine whether to offload, we propose the context-aware decision algorithm to help the system making the right decision. As aforementioned, if system makes a wrong decision, then user cannot save energy and consume more energy.

## Slide 13: Offload? Not Offload?
The decision algorithm should not introduce heavy overhead
We proposed the context-aware decision algorithm to determine whether to offload the computation
  Context is the information of user and mobile device
    CPU usage, network connectivity, etc.
Considered context
  Signal strength
  Throughput
  Time-of-day
  Location

## Slide 14: Why We Use These Four Contexts?
To predict whether offloading has positive or negative impact
To estimate the energy consumption of tasks
  Execution energy and transmission energy
  Throughput and signal strength can be used to model transmission energy
Many factors affect the offloading efficiency
  Data size, transmission time, computation complexity, etc.
  Time-of-day and location may imply the user behaviors and other factors
Image 1
Image 2
Image Processing
The execution time can be very different
Energy Model
Throughput
Signal Strength
Notes: diagram

## Slide 15: Existing Energy Model
Based on PowerTutor[2]
The model assumes a constant power level and may lead to inaccurate estimations
We need a better model
[2] L. Zhang et al. , “Accurate online power estimation and automatic battery behavior based power model generation for smartphones.” In Proc. of International Conference on Hardware/Software Codesign and System Synthesis, 2010.
Notes: Why we need energy model

## Slide 16: Proposed Context-Aware Energy Model
We measure the mobile device’s current flow with Agilent 66321D power meter
Replace communication energy model with our model
Notes: What mobile device we use? We use XE sensation to measure it
The methodology can be applied to any mobile device

## Slide 17: If We Only Have APK Files
APK file is an install file used in Android system
It is not easy to get source code of most of the applications
We develop a tool to help us modifying the third-party applications to offload version
  Analyze and modify the APK files

## Slide 18: APK Analysis Tool Work Flow
We use apktool to decompile/compile the Smali code
  Smali is the register language used in Dalvik VM
Find methods that can be offloaded
Decompile the APK file
Find candidate methods
Smali files
Modify the target method
Compile the modified Smali to APK
Sign the APK file
Modified APK

## Slide 19: Smali Code Example

## Slide 20: Context-Aware Decision Algorithm
Q(T, L) : query database with time T and location L for previous execution cost
  Cost can be execution time or energy consumption
Q(T, L) for cloud and local
Q(null, L) for local/ cloud
If cloud/ local has no record
Do not have record
Execute on cloud/local
If cloud/ local still has no record
Try to execute on cloud/ local
Compare the cost of cloud and local
Try to execute on cloud

## Slide 21: Experiment Setup
HTC one X (client) and android X86 (server)
We recruit 5 users to use the client in a week
HCBS: image transfer and face detection
LCBS: image transfer and color-space conversion
HCSS: nested for-loops
LCSS: simple for-loop
Prediction accuracy, performance gain, overhead

## Slide 22: Decision Accuracy
Take out the first two rounds which are considered as training rounds
At least 80% across all users
At least 80%

## Slide 23: Performance Gain
Most of the executions benefit from cloud executions, and our CADA algorithm successfully identifies the few executions which cannot benefit from cloud
Time improvement
Energy improvement
At least 7X
Notes: At least 7 times imporvement

## Slide 24: Overhead
Space: for each application
Time (runtime): 1 ms
Energy: About 6% energy overhead
This decision algorithm can be implemented in any offloading systems which support dynamic application offloading

## Slide 25: Results of Offloading Third-party Applications
We download four applications from Internet
Packet Chess
  Offload: 1742.5 ms
  Local: 2641.5 ms

## Slide 26: Outline
Introduction
  Efficient Crowdsensing System With Offloading
  Offloading Applications To Cloud
  Contributions
Offloading Applications To Cloud
  Architecture
  Problem Statement
  Algorithm
  Experiments
Offloading Event Analysis Algorithms: Using IsCrowded And IsNoisy As Case Studies
  Implementation
  Case Studies
  Evaluations
Conclusion And Future Work

## Slide 27: System Overview

## Slide 28: Prototype Architecture

## Slide 29: Screenshots

## Slide 30: Event Analysis Algorithms
IsCrowded
  Human detection
  HOG + SVM
    Histogram of Oriented Gradients
  SVM is trained by OpenCV
  We use OpenCV to do the image processing
IsNoisy
  Record the noise by microphone
  Compute the mean db

## Slide 31: HOG Workflow And Example

## Slide 32: Setup
Broker and server
  VMs on Desktop PC
  OS: Android-x86
Client
  HTC smartphone
Database
  MySQL database
We put a PC with dummynet between the broker and client
Network delay = [0, 50, 100, 200, 400] ms
Packet loss rate = [0, 2, 4, 8, 10] %
Bandwidth = [256, 512, 1024, 2048, 4096] kbit/s
We run each setting 5 times

## Slide 33: IsCrowded (Ideal Case)
Offloading use only 56.5% processing time and 25.9% energy consumption

## Slide 34: IsNoisy (Ideal Case)
Offloading uses 235% processing time and 184% energy consumption

## Slide 35: Varying Network Delay
Performance gain
  Time: when delay 50 ms
  Energy: when delay 200 ms

## Slide 36: Varying Packet Loss Rate
Performance gain
  Time: when loss rate 4%
  Energy: when loss rate 8%

## Slide 37: Varying Bandwidth
Performance gain
  Time: when bandwidth 2048 kbit/s
  Energy: when bandwidth 512 kbit/s

## Slide 38: Summary of The Results
The network condition significantly affects the offloading benefit
  Network delay: energy and time (< 50 ms), energy (< 200 ms)
  Packet loss rate: energy and time (< 4 %), energy (< 8 %)
  Bandwidth: energy and time (> 2048 kbit/s), energy (> 512 kbit/s)
Offloading decision is necessary

## Slide 39: Outline
Introduction
  Efficient Crowdsensing System With Offloading
  Offloading Applications To Cloud
  Contributions
Offloading Applications To Cloud
  Architecture
  Problem Statement
  Algorithm
  Experiments
Offloading Event Analysis Algorithms: Using IsCrowded And IsNoisy As Case Studies
  Implementation
  Case Studies
  Evaluations
Conclusion And Future Work

## Slide 40: Conclusion
We strive to minimize the energy consumption and execution time of crowdsensing systems using offloading system
We propose a novel algorithm to determine whether to offload the computation
The accuracy is at least 80%
We develop an APK analysis tool to help us analyze and modify the APK files
We offload third-party applications and show that offloading is feasible in existing applications
We implement a crowdsensing prototype system and show that offloading improves the system performance

## Slide 41: Future Work
Find out other contexts that can have high accuracy for most of the mobile device users and applications
Try to offload methods that contain local resource, for example, camera and GPS.

## Slide 42: Thank You For Your Listening