## Slide 1: ONOS: Towards an Open, Distributed SDN OS
2015/07/20

## Slide 2: Introduction
Open Network Operating System (ONOS)
Distributed architecture
An open source project
Prototype 1:
  Implementing a global network view for scale-out and fault tolerance
Prototype 2:
  Improving performance, notably event latency
  Other new functions
Notes: It provides a global network view to applications, which is logically centralized even though it is physically distributed across multiple servers.

## Slide 3: Challenging requirements
High Throughput: up to 1M requests/second
Low Latency: 10 - 100 ms event processing
Global Network State Size: up to 1TB of data
High Availability: 99.99% service availability

## Slide 4: Prototype 1
global network view
  To manage and share network state across ONOS servers in a cluster
  Each contains switch, port, link, and host information
scale-out
  ONOS runs on multiple servers
  Additional instances can be added to the ONOS cluster to distribute the control-plane workload
fault tolerance
  Continue operating when a component/ONOS instance fails
  Multiple redundant instances waiting to take over
Notes: using several open source building blocks to allow us to quickly validate ideas and explore design possibilities

## Slide 5: Prototype 1
Architecture
Network view data model
manage switch-to-controller mastership
Notes: using several open source building blocks to allow us to quickly validate ideas and explore design possibilities

## Slide 6: Prototype 1: Evaluation
Poor performance and usability
due to the design choices below:
  Consistency and Integrity
  Low Performance and Visibility
    Reacting to a link failure takes up to 30 seconds
  Data Model Issues
    Index maintenance
  Excessive Data Store Operations
    Several network round trips to read/write multiple objects into the data store
  Polling
    Poll the database periodically to detect changes in network state
Notes: adding a switch or flow table entry were slowed down due to several network round trips to read or write multiple objects into the data store.

## Slide 7: Prototype 1: Lessons learned
Design a more efficient data model
Reduce the number of data store operations
Provide fast notifications and messaging across nodes
API needs to be simplified to represent the network view abstraction

## Slide 8: Prototype 2
RAMCloud Data Store
  Replaced the 1st prototype’s graph database stack
  Low latency (e.g. remote read/write latency in the 15-30 µs)
Optimized Data Model
  Minimized the number of references between elements
  Fewer read/write operations for each update

## Slide 9: Prototype 2
Topology Cache
  Topology information is updated infrequently but is read-heavy
  Keeping it in memory on each instance
Event Notifications
  To solve polling problem
  Such as topology change, flow installation and packet-out
Network View API
  Replace the generic Blueprints graph API

## Slide 10: Prototype 2
Architecture

## Slide 11: Prototype 2: Evaluation
(1) Basic Network State Changes
  Latency for adding a switch (Ser. = Serialization, Des. = Deserialization; Unit: ms)
 | Read | Write | Ser. | Des. | Other | Total
1. Generic Graph Data Model | 10.1 | 3.5 | 7.2 | 0.93 | 0.56 | 22.2
2. New Data Model | - | 0.28 | 0.89 | - | 0.17 | 1.19
3. (2)+Proto. Buf. | - | 0.23 | 0.01 | - | 0.06 | 0.244
4. (3)+Infiniband | - | 0.08 | 0.01 | - | 0.06 | 0.099

## Slide 12: Prototype 2: Evaluation
(2) Reaction to Network Events
  End-to-end latency of the system for updating network
  Latency for Rerouting 1000 Flows
Latency | Median | 99th %ile
Latency to the 1st FlowMod | 45.2 ms | 75.8 ms
Total Latency | 71.2 ms | 116 ms

## Slide 13: Prototype 2: Evaluation
(3) Path Installation
  Path Installation Latency
 | Median | 99th %ile
Latency to the 1st FlowMod | 34.1 ms | 68.2 ms
Total Latency | 53.1 ms | 97.9 ms