## Slide 1: OpenFlow: Enabling Innovation in Campus Networks
ACM SIGCOMM 2008

## Slide 2: The Need for programmable networks
Introduction

## Slide 3: The Need For Programmable Networks
Today, there is almost no practical way to experiment with new network protocols
  The scale is not big enough to gain confidence
  Kind of a vicious circle
Virtualized programmable networks could lower the barrier to entry for new ideas.
Networking community is working on a nationwide solution
  Such as GENI
  But it’ll take years to deploy

## Slide 4: The Need For Programmable Networks
This paper focus on a shorter-term question
  “As researchers, how can we run experiments in campus network?”
Goal: purpose a new switch feature that extend programmability
  Commercial solutions are too closed, inflexible
  Research solutions either have insufficient performance/fanout, or are too expensive

## Slide 5: The Need For Programmable Networks
Solution: compromise on generality
  Amenable to high-performance and low-cost implementations
  Capable of supporting a board range of research
  Assured to isolate experimental traffic from production traffic
  Consistent with vendors’ need for closed platforms

## Slide 6: The openflow switch

## Slide 7: The Openflow Switch
Most Ethernet switch contain flow-tables
  Typically built from TCAMs, run at line-rate
  Identify a common set of function and exploit them
Openflow is an open protocol to program the flow-table in different switches and routers
  Network administrator can isolate experiment traffic from regular ones
  Researcher can control their own flow

## Slide 8: The Openflow Switch
Consist of at least three parts
  A flow table
    with an action associated with each entry
  A secure channel
    Connects the switch with a remote control process(Controller)
  The OpenFlow Protocol

## Slide 9: The Openflow Switch

## Slide 10: Flow Entry in Flow Table
Packet header
  10-tuple in first generation “Type 0” switch
  Each field can be a wildcard
Associated action
Statistics
  # of packet, bytes for each flow…etc.

## Slide 11: Associated Action
A: Forward this flow’s packet to a given port(s)
  Allow packets to be routed through the network
B: Encapsulate and forward to a controller
  Delivered to secure channel
  Typically for the first packet in a flow
C: Drop this flow’s packets
D: Forward this flow’s packets through normal processing pipeline

## Slide 12: Associated Action
Dedicated OpenFlow switches
  A dumb datapath element that forwards packets between ports, as defined by remote controller
  Support action A to C
OpenFlow-enabled switches
  A functional router/switch that’s enhanced with OpenFlow
  Reuse some of it’s hardware(such as TCAMs)
  Support action A to C
  Support action D or use VLANs to differentiate

## Slide 13: OpenFlow-enabled Switch

## Slide 14: Associated Action
Those that supports the minimum required action mentioned earlier is called “type 0” switch.
Some switch will support some extra features, these are called “type 1” switch.

## Slide 15: Controller
A controller adds and removes flow-entries
A simple static controller
  Just establish flows to interconnect a set of test computers for the duration of the experiment
  Isolate experimental traffic from normal ones
  Generalization of VLANs
There can be some more sophisticated controllers
  Dynamically add/remove flows in the progress of the experiment
  Share the network between multiple researchers

## Slide 16: Using OpenFlow

## Slide 17: Using OpenFlow
Ex: Amy want to test her new Amy-OSPF routing protocol
The Amy-OSPF will run in a controller
Each time a new flow starts, the Amy-OSPF will pick a route
All the following packets will be forwarded accordingly
Amy can limit this action only to the packet coming from her own computer’s port

## Slide 18: Using OpenFlow
Question: can such a centralized controller be fast enough to process new flows and program the Flow Switches?
A part of this question is answered in Ethane prototype(ACM SIGCOMM 2007)
A low-cost commodity PC can handle over 10000 new flows per second
  Enough for campus

## Slide 19: Experiments in a Production Network
Two important properties
  Packets belonging to other users should be routed normally
  Amy should only be able to add flow entries for the traffic she is allowed to control
First one is achieved by OpenFlow-enabled switches
Second one depends on controller implementation

## Slide 20: Some more examples
Network Management and Access control
VLANs
Mobile wireless VOIP clients
  User a controller that track the user’s location, and do the handoff by changing the flow-tables
Non-IP network
  Can use Ethernet header, Ethernet type or new non-IP protocols

## Slide 21: Some more examples
Processing packets rather than flows
  Forward every packets to controller at the cost of performance
  Route them to a programmable switch, such as NetFPGA

## Slide 22: Conclusion
OpenFlow is a pragmatic compromise
  Allow researches to run experiments on heterogeneous switches and routers in a uniform way
  Vendors don’t have to expose their internal working
  Researchers don’t have to write vendor-specific programs
Hoping that new generation of control software will emerges
Accelerating the innovation in networking

## Slide 23: Backup Slides
What is VLAN?
http://s90304a123.pixnet.net/blog/post/38793827-ccna%E6%95%99%E5%AD%B8-vlan