## Slide 1: TCP in Wireless Environments: Problems and Solutions
YE TIAN, KAI XU, AND NIRWAN ANSARI

## Slide 2: Introduction
TCP and IP reside in the different layers of the open system interconnection (OSI) architecture
IP
  Connectionless best-effort based variable length packet delivery network layer protocol
   reliable, timely, in-order delivery
  Routing mechanism based on the addressing scheme
TCP
  layer four transport protocol that uses the basic IP services
  connection-oriented packet transport mechanism that ensures the reliable and ordered delivery of data

## Slide 3: TCP packets
Sequence number
ACKs with sequence numbers of the next expected packets → successfully received in-order packets
Failures
  flow control and congestion control algorithms based on the sliding window and additive increase multiplicative decrease (AIMD) [1] algorithms

## Slide 4: TCP Reno
Slow start
  cwnd is increased by 1 MSS for every ACK received (grows exponentially in round-trip times)
  When cwnd reaches ssthresh, the TCP sender enters the congestion avoidance phase
Congestion avoidance
  employs a sliding-window-based flow control mechanism
  CWND+=1/CWND upon reception of an ACK(linearly)
Fast recovery/fast retransmit
  Reduces the size of its congestion window (cwnd) to half and linearly increases cwnd as in congestion avoidance

## Slide 5: Challenges in the Heterogeneous Network
Future all-IP networks will most likely be heterogeneous, but the TCP exhibits weaknesses in such hybrid environments
Degradation of throughput, inefficiency in network resource utilization, and excessive interruption of data transmissions

## Slide 6: Challenges in the Heterogeneous Network (cont.)
Wireless links
  weather conditions, urban obstacles, multipath interferences, large moving objects, and mobility of wireless end devices → much higher BERs
  limitations of radio coverage and user mobility require frequent handoffs → temporal disconnections and reconnections between the communicating end hosts during a communication session

## Slide 7: Challenges in the Heterogeneous Network (cont.)
A short disconnection event can actually stall the TCP transmission for a much longer period

## Slide 8: Challenges in the Heterogeneous Network (cont.)
Multiple unsuccessful retransmissions within one RTT would cause the retransmission timer to exponentially back off

## Slide 9: Challenges in the Heterogeneous Network (cont.)
Link asymmetry
  A sender could mistakenly interpret a bad reverse channel condition as congestion on the forward channel and unnecessarily reduce the sending rate → TCP performance degradation
  ACK compression effect
    The queuing in the reverse path of a TCP flow can cause the almost instantaneous arrival of successive ACKs at the sender end
    → break TCP’s self-clocking and cause long bursts of packet transmission in the forward direction, and thus possible congestive packet losses

## Slide 10: Challenges in the Heterogeneous Network (cont.)
Mobile wireless communications
  User mobility as well as limited radio frequency coverage of wireless devices, either base stations or terminals → Handoff
Wireless ad hoc network
  Infrastructurelessness and high node mobility of the network → frequent route changes and network partitions
Satellite network
  long propagation delay → long-range transmission inefficient

## Slide 11: TCP for Different Wireless Applications
Satellite Networks
Ad Hoc Networks
Cellular Network

## Slide 12: Satellite Networks
Takes the sender of a TCP connection a fairly long time to reach a high sending rate during the traditional slow start phase
TCP-Peach
  Sudden start (slow start)
    The reception of ACKs for the dummy packets indicates the availability of the unused network resource
    Dummy packets are labeled with low priority → a router would drop the dummy packets first in the event of congestion
  Rapid recovery (fast recovery)
    Improve throughput in the presence of high link error rate
    The sender uses the lower-priority dummy packets to interleave the data packets and inflates the sending window size upon receptions of ACKs for the dummy packets

## Slide 13: Ad Hoc Networks
High error rate and frequent route changes and network partitions are typical
ATCP
  Implemented as a thin layer inserted between the standard TCP and IP layers
  Explicit congestion notification (ECN) to detect congestion and distinguish congestion loss from error loss
  ICMP Destination Unreachable message to detect a change of route or temporary partition in an ad hoc network

## Slide 14: Ad Hoc Networks (cont.)
The ATCP layer puts the TCP sender into either the persist, congestion control, or retransmit state accordingly
  High BER - ATCP retransmits the lost packet so that TCP does not perform congestion control
  A route change or network partition - ATCP puts the TCP sender into the persist state waiting for the route to reconnect
  Packet reordering - ATCP reorders the packets so that TCP would not generate DUPACKs
  Real congestion - TCP enters the normal congestion control stage

## Slide 15: Cellular Network
Handoff and high BER
Freeze-TCP
  Only requires code modifications at the mobile unit or receiver side
  The mobile unit has knowledge of the radio signal strength, and therefore can predict the impending disconnections
  In the presence of impending disconnection
    Receiver proactively sets the advertised window size to zero → ceases sending more packets while keeping its sending window unchanged
    Reconnection - the transfer can resume quickly at the rate before the disconnection occurs

## Slide 16: Implementation of Wireless TCP
Split Mode
  Divides the TCP connection into wireless and wired portions, and ACKs are generated for both portions separately
  The performance on the wired portion is least affected by the relatively unreliable wireless portion
End-to-End Approach
  Treats the route from the sender to the receiver as an end-to-end path

## Slide 17: Split Mode
Both end hosts communicate with the intermediate router independently without knowledge of the other end
I-TCP
  The congestion window is maintained separately for the wireless and the fixed connections

## Slide 18: End-to-End Approach
Only the end hosts participate in flow control
The receiver provides feedback reflecting the network condition, and the sender makes decisions for congestion control

## Slide 19: End-to-End Approach (cont.)
The ability to accurately probe for the available bandwidth is the key to better performance
  Minimum unused link capacity of the flow’s fair share along the path
Congestion control mechanism
  Reactive Congestion Control
    The sender rectifies the congestion window when the network situation becomes marginal or has crossed a threshold
  Proactive Congestion Control
    Feedbacks from the network guide the sender to reallocate network resources in order to prevent congestion

## Slide 20: Reactive Congestion Control
The congestion window is adjusted based on the collective feedback of ACKs and DUPACKs generated at the receiver
  continuously increasing the congestion window gradually until the network reaches the congestion state → TCP fall back to a much slower transmission rate, which may be unnecessary for wireless random loss

## Slide 21: Reactive Congestion Control (cont.)
The fast recovery algorithm of Reno takes care of a single packet drop within one window
New Reno
  The fast recovery mechanism does not terminate until multiple losses, indicated by the reception of partial ACKs, from one window are all recovered
TCP SACK
  It indicates a block of data that has been successfully received and queued at the receiver when packet loss occurs instead of sending a partial ACK
  SACK requires modifications at the sender and receiver sides

## Slide 22: Proactive Congestion Control
Adjust the congestion window proactively to an optimal rate according to the information collected via feedback
TCP Vegas
  Estimates the backlogged packets in the buffer of the bottleneck link
  Selects the minimal RTT as a reference to derive the optimal throughput the network can accommodate
  The difference between the optimal throughput and the actual sending rate can be used to derive the amount of backlogged data in the network
Sets two thresholds of backlogged data

## Slide 23: Proactive Congestion Control(cont.)
TCP Veno
  Adopts the same methodology as Vegas to estimate the backlogged packets in the network
  Differentiate the cause of packet loss
    Below a threshold, the loss is considered to be random → increases the congestion window in a conservative manner
    Above a threshold, the loss is congestive → adopts the standard Reno scheme

## Slide 24: Proactive Congestion Control(cont.)
TCP Westwood
  Deploys an available bandwidth measurement module at the sender side based on the interval of returning ACKs
  Congested - sets the slow start threshold to reflect its estimated bandwidth-delay product
  Claims improved performance over TCP Reno and SACK while achieving fairness and friendliness
  Requires minimum modification at end hosts, and in some cases also the routers

## Slide 25: Proactive Congestion Control(cont.)
TCP-Jersey
  Available bandwidth estimation (ABE) - continuously estimates the bandwidth available to the connection and guides the sender to adjust its transmission rate when the network becomes congested
  Congestion warning (CW) - routers alert end stations by marking all packets when there is a sign of incipient congestion (ECN)
  Calculates the optimum congestion window size at the sender

## Slide 26: Proactive Congestion Control(cont.)
  Proactive schemes, in general, exhibit the ability to handle random loss more effectively
    Proactive schemes are able to better distinguish random loss from congestive loss than reactive schemes

## Slide 27: Summary
Illustrating the typical wireless TCP techniques with examples
It is difficult to make an overall conclusive evaluation of one solution vs. another