## Slide 1: Video Streaming Using a Location-based Bandwidth-Lookup Service for Bitrate Planning
Haakon Riiser, Rore Endestad, Paul Vigmostad,
Netview Technology AS, Norway

## Slide 2: Introduction
Problem: severe bandwidth fluctuations & networks unresponsive
Solution: receivers equipped with a GPS
  Download rate is constantly monitored
  Central database (GPS positional data)
Notes: 無線網路的問題有 : 嚴重的頻寬波動 & 網路幾分鐘無反應，這些都會造成視頻的品質影響
Video streaming的接收器上裝有GPS，下載速度被監控，GPS週期性回傳位置給central database

## Slide 3: Location-based Bandwidth Lookup Service
It enables all users to query for predicted available bandwidth for given locations based on previous observations
More stable video
  Pre-buffering
  Early quality adaption
Notes: 可以讓所有可以去查詢 將來可用的頻寬(以位置為基礎)

## Slide 4: Bandwidth Monitoring(1/5)
Information
  User’s actual location
  Intended destination
  Route
  Expected bandwidths
Four different types
  Metro railway
  Bus
  Ferry
  Tram

## Slide 5: Bandwidth Monitoring(2/5)
Choosing a low video bitrate before entering the tunnels, pre-buffering enough video to last through the tunnels
Notes: 進入地下隧道時，訊號微弱，先切換低成的bitrate，預先儲存到buffer裡

## Slide 6: Bandwidth Monitoring(3/5)
The average values vary greatly
GPS satellites

## Slide 7: Bandwidth Monitoring(4/5)
Available bandwidth varies quite a lot
The signal is never completely gone
The signal is strongest when the ferry is close to land

## Slide 8: Bandwidth Monitoring(5/5)
Above the bus route
predictable
downslope

## Slide 9: Video Streaming With A GPS-based Bandwidth-lookup Service
route
average bandwidth
standard deviation

## Slide 10: Algorithm(1/3)
A buffer-based reactive algorithm
Select the video bitrate based on the number of seconds of video that are preloaded in the buffer
Shortcoming
  Quality oscillations
  Network outages

## Slide 11: Algorithm(2/3)
A history-based prediction algorithm
For every 100 meters along the path, the system queries for a predicted bandwidth(average of historical bandwidth)
Shortcoming
  Accuracy of GPS signal
  Competition for bandwidth
  Base station failure

## Slide 12: Algorithm(3/3)
An omniscient prediction algorithm
Optimal result
This a posteriori algorithm has all measurements for a particular test run available

## Slide 13: Bandwidth Capping
Notes: 預測頻寬選擇+-10%較好，可以避免劇烈波動&buffer underruns

## Slide 14: Scaling the buffer step size relative to video bitrate

## Slide 15: Removing rapid oscillations in quality
Having slightly different step sizes when going up in quality than when going down

## Slide 16: Combination with the reactive algorithm
Both algorithms select a quality level, and choose the lower one

## Slide 17: Variable-length travel handling

## Slide 18: Simulation(1/3)

## Slide 19: Simulation(2/3)

## Slide 20: Simulation(3/3)

## Slide 21: Real World Video Streaming Tests

## Slide 22: Discussion and Open Issues
Time of day
Day of week
Competition for bandwidth
Direction and speed is unpredictable(cars)