## Slide 1: A Blind Streaming System for Multi-client Online 6-DoF View Touring
ShengMing (shengming0308@gapp.nthu.edu.tw) Advisor: Cheng-Hsin Hsu Networking and Multimedia Systems Lab, CS, National Tsing Hua University
NMSL@NTHU
Networking and Multimedia Systems Lab

## Slide 2: Outline
Inspiration
Goal & Challenges
Related Work
System Design
Novel View Optimization
Cloud Service Provider
  Pose Predictor
  Candidate Generator
  Coverage Estimator
  Solver & Algorithms
Implementation
Evaluations
Conclusion & Future Work

## Slide 3: Intellectual Property Leakage
Inspiration
3D content (mesh)
Mesh based
Content leakage
Content creators
RGB-D images based
RGB-D images
Content creators
6-DoF clients
6-DoF clients
We only reveal partial 3D content by images!

## Slide 4: Bandwidth Saving and No Mesh Streaming
Inspiration
view streams
Frame-by-Frame Streaming
Content creators
RGB-D source view (image) based
small number of source views
Content creators
6-DoF clients
6-DoF clients
…
Only sends a small number of source views to serve many clients

## Slide 5: Novel View Synthesis
RGB source views
  Describe color information
D source views
  Describe partial content geometry
Inspiration
?
Color
Geometry
Novel view synthesizer
Limitations
  Not light enough to run on Head Mounted Displays (HMDs) in real-time
Reference View Synthesizer (RVS)[RVS]
[RVS] Bart Kroon and Gauthier Lafruit. 2018. Reference View Synthesizer (RVS) 2.0 manual. Taipa, Macao

## Slide 6: Outline
Inspiration
Goal & Challenges
Related Work
System Design
Novel View Optimization
Cloud Service Provider
  Pose Predictor
  Candidate Generator
  Coverage Estimator
  Solver & Algorithms
Implementation
Evaluations
Conclusion & Future Work

## Slide 7
Challenges:
Goal & Challenges
Goal:
Synthesize high quality views for all clients
Constraints:
Source view budgets (no. of source views allowed)
Content observation budgets
Blurred
View Requests
No direct access to 3D content
No close form representation of quality prediction
??
Defense against Structure-from-Motion

## Slide 8: Outline
Inspiration
Goal & Challenges
Related Work
System Design
Novel View Optimization
Cloud Service Provider
  Pose Predictor
  Candidate Generator
  Coverage Estimator
  Solver & Algorithms
Implementation
Evaluations
Conclusion & Future Work

## Slide 9: Novel View Synthesis
Hladky et al. invented QuadStream to synthesize view within a pre-defined view cell
  Requires 3D content
Choi et al. generalized scalar depth prediction from multiple cameras to refine synthesized views
Attal et al. transform stereo videos to multi-sphere images to synthesize 6-DoF views
Related Work
Jozef Hladky, Michael Stengel, Nicholas Vining, Bernhard Kerbl, Hans-Peter Seidel, and Markus Steinberger. 2022. QuadStream: A Quad-Based Scene Streaming Architecture for Novel Viewpoint Reconstruction. ACM Transactions on Graphics 41, 6 (November 2022), 1–13.
Inchang Choi, Orazio Gallo, Alejandro Troccoli, Min Kim, and Jan Kautz. 2019. Extreme View Synthesis. In Proc. of IEEE/CVF International Conference on Computer Vision (ICCV’19). Seoul, Korea.
Benjamin Attal, Selena Ling, Aaron Gokaslan, Christian Richardt, and James Tompkin. 2020. MatryODShka: Real-time 6DoF video view synthesis using multi-sphere images. In Proceedings of European Conference on Computer Vision (ECCV’20). Glasgow, United Kingdom, 441–459
1.
2.
3.

## Slide 10: Coverage optimization
Suresh et al. solved 2D terrain coverage problem
  Greedy based, discretized pose
Abu-Ghazaleh maximized the number of covered targets given a fixed number of cameras
Peng and Isler computed optimal flying paths for aerial 3D reconstruction
Related Work
Sumi Suresh, Athi Narayanan, and Vivek Menon. 2020. Maximizing Camera Coverage in Multicamera Surveillance Networks. IEEE Sensors Journal 20, 17 (September 2020), 10170–10178
Vikram Munishwar and Nael Abu-Ghazaleh. 2010. Scalable Target Coverage in Smart Camera Networks. In Proc. of ACM/IEEE International Conference on Distributed Smart Cameras (ICDSC’10). Atlanta, GA, 206–213.
heng Peng and Volkanr Isler. 2019. Adaptive View Planning for Aerial 3D Reconstruction. In Proc. of IEEE International Conference on Robotics and Automation (ICRA’19). Montreal, Canada, 2981–2987.
3.
2.
1.

## Slide 11: Outline
Inspiration
Goal & Challenges
Related Work
System Design
Novel View Optimization
Cloud Service Provider
  Pose Predictor
  Candidate Generator
  Coverage Estimator
  Solver & Algorithms
Implementation
Evaluations
Conclusion & Future Work

## Slide 12: Blind Streaming
6-DoF clients
  Transmit pose trajectories
    Pairs of position & orientation
  Novel view synthesis
Cloud service provider
  Collect pose trajectories
  On behalf of 6-DoF clients
  Novel view optimization algorithms
Content creator
  Serve view requests
System Design

## Slide 13: Component Diagram of Each Party
Probing view: Low resolution depth image (1/16 of original)
System Design
Update source views every second

## Slide 14: Outline
Inspiration
Goal & Challenges
Related Work
System Design
Novel View Optimization
Cloud Service Provider
  Pose Predictor
  Candidate Generator
  Coverage Estimator
  Solver & Algorithms
Implementation
Evaluations
Conclusion & Future Work

## Slide 15: Summation of Expected Quality over Novel Views and 6-DoF clients
Novel View Optimization
source view budgets
probing view budgets
for all clients and all novel views
expected quality of a novel view v
choose the optimal set of source views

## Slide 16: Outline
Inspiration
Goal & Challenges
Related Work
System Design
Novel View Optimization
Cloud Service Provider
  Pose Predictor
  Candidate Generator
  Coverage Estimator
  Solver & Algorithms
Implementation
Evaluations
Conclusion & Future Work

## Slide 17: Compensate for Latency
Take history pose trajectory to predict future ones
Compute source views beforehand
Pose Predictor
S. Gul, S. Bosse, D. Podborski, T. Schierl, and C. Hellge. Kalman filter-based head motion prediction for cloud-based mixed reality. In Proc. of ACM International Conference on Multimedia (MM’20), page 3632–3641, Seattle, WA, October 2020
X. Hou and S. Dey. Motion prediction and pre-rendering at the edge to enable ultralow latency mobile 6dof experiences. IEEE Open Journal of the Communications Society, 1:1674–1690, 2020
Mature work
  Kalman filter based (Serhan et al.)
  LSTM based (Hou et al.)
Assume perfect prediction
history
predicted

## Slide 18: Outline
Inspiration
Goal & Challenges
Related Work
System Design
Novel View Optimization
Cloud Service Provider
  Pose Predictor
  Candidate Generator
  Coverage Estimator
  Solver & Algorithms
Implementation
Evaluations
Conclusion & Future Work

## Slide 19: Tradeoff between Runtime and Optimality
Procedure:
Concatenate all poses from all 6-DoF clients
Cut partitions from the concatenated pose trajectory
Generate a source view candidate from each partition
  Candidates as representatives (leverage temporal locality)
  The pose at least covers nearby poses
Candidate Generator
concatenated poses
poses
poses
poses
...
candidate generation
p
p
p
p
p
...
p
p
0
1
2
3
.
.
4
...
To be determined:
How many partitions (poses) should we have?
How to generate a candidate from a partition?
How many ?
How?
19

## Slide 20: Strike Optimal Number of Partitions (Step 1)
Random arbitrary-number selection Analysis
(Relaxed to selection of source views)
  are no. of source views and partitions
  , redundant factor
  , source view budget
  , computational load
  , candidate overhead + computational load
Select M candidates out of P poses at random
  Always assume N optimal candidates are among P poses
Candidate Generator
0
P seats
Seats for M candidates
1
2
3
4
5
.
.
.
P-1
0
an optimal pose
pick one of them
…

## Slide 21: Strike Optimal Number of Partitions (Step 2)
Random arbitrary-number selection Analysis
2. N optimal ones are included in the N+ source views
  A candidate is selected if it says an “yes”
  of an optimal source view is a linear function of
    , when
    , when
  of a sub-optimal source view is not important
Candidate Generator
0
Seats for M candidates
1
2
3
4
5
.
.
.
M-1
says an “yes” or “no”
0
1
3
.
.
.
2
4
.
.
.
yes
no
N+ source views

## Slide 22: Strike Optimal Number of Partitions (Step 3)
Derived from
Random arbitrary-number selection Analysis
3.
  Select M candidates out of P poses at random & N optimal ones are included in the N+ source views
  Maximize with respect to
  Constraint:
as
Candidate Generator
  are no. of source views and partitions
  , redundant factor
  , source view budget
  , computational load
  , candidate overhead + computational load
Such policy is used for deriving
m, h are constant in an experiment

## Slide 23: Strike Optimal Number of Partitions
Random arbitrary-number selection analysis to determine
(Relaxed to selection of source views)
  are no. of source views and partitions
  , redundant factor
  , source view budget
  , computational load
  , candidate overhead + computational load
Select M candidates out of P poses at random
Select source views from M candidates
as
Candidate Generator
concatenated poses
poses
poses
poses
...
candidate generation
p
p
p
p
p
...
p
p
0
1
2
3
.
.
4
...
How many ?
m, h are constant in an experiment

## Slide 24: Generate a Candidate from a Partition
Consider position and orientation separately
Average pose of a partition of size as a candidate
: average position =
  Vector mean
: average orientation =
  Unit quaternion to avoid rotation order ambiguity
  Solve a maximum eigenvalue problem of a 4x4 matrix
Candidate Generator
concatenated poses
poses
poses
poses
...
candidate generation
p
p
p
p
p
...
p
p
c
c
c
c
c
c
c
...
How?
is the length of a partition

## Slide 25: Outline
Inspiration
Goal & Challenges
Related Work
System Design
Novel View Optimization
Cloud Service Provider
  Pose Predictor
  Candidate Generator
  Coverage Estimator
  Solver & Algorithms
Implementation
Evaluations
Conclusion & Future Work

## Slide 26: Mesh Creation
Create a image plane mesh of WxH vertices seen from
Move the vertices along the projection lines according to their depth
Vertex connections are kept
  Linear interpolation of depth between vertices
Transform the mesh to
Coverage Estimator
image plane mesh
projection lines
linear interpolation

## Slide 27: Disocclusion Removal
Analyze how covers
Values in should be consistent with unless:
does not cover that pixel Infinity depth
That part is disoccluded
Disocclusion removal:
Compute
Remove those threshold in
Coverage Estimator
Colored parts from
Gray parts are disocclusion
Color view

## Slide 28: Compute Coverage Map of on ,
Coverage Estimator
For a pair of candidates:
Request depth images, and
Create mesh from
Re-project to as
Remove disocculusion of by comparing with
For all pairs of candidates:
Repeat the procedure of computing for all candidates
Result in probing views (low resolution depth images)

## Slide 29: Outline
Inspiration
Goal & Challenges
Related Work
System Design
Novel View Optimization
Cloud Service Provider
  Pose Predictor
  Candidate Generator
  Coverage Estimator
  Solver & Algorithms
Implementation
Evaluations
Conclusion & Future Work

## Slide 30: Pixel Contribution Function
Describe contribution of a pixel:
for
: coverage count
Zero coverage:
Bounded quality:
Monotonic increase: for
Quality saturation: for
Solver
We don’t use Boolean modeling:
for
for
because we seek for improvement from multiple coverage
Saturates fast and bounded

## Slide 31: Optimization Objective
Solver
: coverage map of how covers
: Boolean decision variables
  indicates the candidate is selected
: weighting mask (averaging mask)
: element-wise multiplication and summation
coverage count of
matrix version of
average over all candidates
select or not
source view budget
We will call it value in the following discussion

## Slide 32: Uniform Solver (Uni)
Pick candidates every fixed skips
Guarantees uniform source view distribution across temporal axis and 6-DoF clients
No need for coverage estimation
Runs fast
Solver
0
1
2
3
.
.
4
.
5
✔
✔
✔
Source view candidates

## Slide 33: Branch & Bound Solver (BB)
Start from , mark all as “undetermined”
value of setting all “undetermined” to 1
Branch
  Set one of the 0s to 1 such that value increases the most
  Mark the corresponding 0 in Branch 1. as “determined”
Bound
  value of the best sequence
  Remove from list if
Solver
set to 1
set to 0
Their upper bounds

## Slide 34: Uniform & Modify Solver (UM)
Start from
Always iterate in the terminal sequences
  Terminal sequence:
Clear-than-set iteration
  Clear one of the 1s to 0 such that value decreases the least
  Set one of the 0s to 1 such that value increases the most
  Duplicated are ignored
Solver
A terminal sequence
Clear
Set

## Slide 35: Component Diagram of Each Party
Probing view: Low resolution depth image (1/16 of original)
System Design
Update source views every second

## Slide 36: Outline
Inspiration
Goal & Challenges
Related Work
System Design
Novel View Optimization
Cloud Service Provider
  Pose Predictor
  Candidate Generator
  Coverage Estimator
  Solver & Algorithms
Implementation
Evaluations
Conclusion & Future Work

## Slide 37: Testbed
Render depth images using an Open3D renderer
Offload RVS synthesizer to PC
Unity Engine as high quality source view provider
Implementation

## Slide 38: Outline
Inspiration
Goal & Challenges
Related Work
System Design
Novel View Optimization
Cloud Service Provider
  Pose Predictor
  Candidate Generator
  Coverage Estimator
  Solver & Algorithms
Implementation
Evaluations
Conclusion & Future Work

## Slide 39: Comparison Algorithms / Candidate Generator (IXR’22)
Content creator provides scalar coverage ratio from a pose to another
S-Cdd
  Generate a candidate if a pose cannot cover 75+% of the previous candidates
C2I: Integer programming solver
C2G: Greedily select the best 2 candidates at a time
Opt
  Select all the source views
  Highest performance given candidates
source view budgets
Evaluations
: Boolean column vector denote a selection
Matrix approximation of set union operations

## Slide 40: Setup
Content
House
Big Room
Small Room
Default parameters
Number of 6-DoF clients = 16
Source view budgets
Candidates
Solver
Candidate generator S-Cdd, proposed
Quality Metrics
Peak Signal to Noise Ratio (PSNR) =
Structural Similarity (SSIM)
Video Multi-Method Assessment Fusion (VMAF)
Device specification
CPU: AMD Ryzen 7 5700X 8-core
GPU: NVIDIA Geforce RTX 3090 Ti
SSIM
Evaluations

## Slide 41: Sample results
Best frame in PSNR from a random synthesized video
Worst frame in PSNR from a random synthesized video
Artifacts: blur, distortion
Evaluations
See demo videos

## Slide 42: Quality Saturates as increases
Quality saturates when
VMAF performs relatively worse
  Our formulation does not consider temporal continuity
Evaluations

## Slide 43: Bandwidth Reduction
H.264 encoder, quantization parameter (QP) = 0
Encode ground truth video at 50 fps
Encode source views separately
Save 94% of bandwidth consumption
Evaluations

## Slide 44: Solver Comparison
C2I, C2G only have scalar coverage ratio information
Uni, BB, UM outperform C2I, C2G
Uni, UM seek for improvement over Uni in PSNR
Evaluations

## Slide 45: Candidate Generator Comparison
Solver = UM
Proposed generator consistently outperforms S-Cdd
Proposed generator feeds high quality inputs to the pipeline
Evaluations

## Slide 46: Runtime Distribution
Solver = UM
Number of iterations = 128
Candidate generator runs fast
Coverage estimator is implemented in CPU
Solver is implemented in GPU
  Frequently evaluate value
Evaluations

## Slide 47: Outline
Inspiration
Goal & Challenges
Related Work
System Design
Novel View Optimization
Cloud Service Provider
  Pose Predictor
  Candidate Generator
  Coverage Estimator
  Solver & Algorithms
Implementation
Evaluations
Conclusion & Future Work

## Slide 48: Defense against Structure-from-Motion (SfM)
Colmap
  J. L. Schonberger and J.-M. Frahm. Structure-from-motion revisited. In ¨ Proc. of IEEE Conference on Computer Vision and Pattern Recognition (CVPR’16), Las Vegas, NV, June 2016.
720 color images with 960x540 resolution, 10+ GPU hours
Conclusion & Future Work

## Slide 49: Remarks
Conclusion
  Propose a content creator friendly blind streaming system
  Compute coverage maps without access to 3D content
  Improve quality by 2.27 dB in PSNR, 12 in VMAF compared to scalar coverage ratio blind streaming system
Future work
  Parallelism in frequently-evaluated values
  Employ real-time view synthesis in HMDs
  Formulate optimization objective that considers temporal continuity
Conclusion & Future Work

## Slide 50: Thank you for your attention!
Publications:
S. Tang, Y. Sun, J. Fang, K. Lee, C. Wang and C. Hsu, ”Optimal Camera Placement for 6 Degree-of-Freedom Immersive Video Streaming Without Accessing 3D Scenes”, in Proc. of Interactive eXtended Reality (IXR’22), Lisbon, Portugal, October 2022.
S. Tang, C. Hsu, Z. Tian, and X. Su, ”An Aerodynamic, Computer Vision, and Network Simulator for Networked Drone Applications”, in Proc. of ACM Annual International Conference on Mobile Computing and Networking (MobiCom’21), New Orleans, USA, February 2022, Poster Paper.
Y. Sun, S. Tang, C. Wang, and C. Hsu, ”On Objective and Subjective Quality of 6DoF Synthesized Live Immersive Videos”, in Proc. of ACM Multimedia Workshop on Quality of Experience in Visual Multimedia Applications (QoEVMA’22), Lisbon, Portugal, October 2022.
Sheng-Ming Tang (shengming0308@gapp.nthu.edu.tw)
Thanks for the help of Prof. Hsu, the committees,
Ching-Ting Wang, Yuan-Chun Sun, Jia-Wei Fang, Kuan-Yu Lee, and all lab mates.